## Slide 1: WF on guidelines for Rel-17 FR1 CA/DC band combinations approval handling
Apple Inc., Skyworks Solutions Inc.
3GPP TSG-RAN #91-e
Electronic Meeting, March 16th – 26th
RP-210892

## Slide 2: Background
UE band combination basket work items block approval process has been implemented since LTE and continued in NR.
The framework has successfully facilitated the TR TP review process and improved RAN4 work efficiency on developing the UE RF requirements for majority of band combinations.
Nonetheless, there are certain band combinations which may require additional technical justifications or requirements not covered by the standard basket TR TP format and may not be suitable for block approval process.
This contribution is intended to provide guidelines for FR1 band combinations approval handling.

## Slide 3: Guidelines for Combinations Not for Block Approval
Intra-band contiguous EN-DC with new bandwidth class, such as classes AC and CB: Need a new feature defined.
Intra-band UL CA with 2 CCs where A-MPR requirements have not been specified (in basket WID not for block approval)
Intra-band contiguous UL CA with 3 CCs (feature not yet defined)
UL CA with three or more non-contiguous CCs (feature not yet defined) including
  Inter-band UL CA with UL in three or more bands
  Intra-band non-contiguous UL CA with three or more discrete UL CCs
  Inter-band UL CA consisting of intra-band non-contiguous UL CA

## Slide 4: Way Forward
Guidelines for Rel-17 FR1 CA/DC combinations approval that RAN4 will develop should be captured in the TR created in the SI on band combination handling.
The list of guidelines presented in this WF can be used as baseline for further discussions and refining in coming RAN4 meetings.
Dedicated agenda in coming RAN4 meetings can be arranged by RAN4 Chairman for guidelines which require further discussions.