## Slide 1
Agenda item: 7.2.5.1 Source: Apple Inc. Title: Discussion on cancellation and replacement for eURLLC
Document for: Discussion and Decision
3GPP TSG RAN WG1 Meeting #101-e R1-2004985
E-meeting, 25 May – 5 June, 2020

## Slide 2
Background
  Cancellation and replacement has been under discussion in RAN1. For PUSCHs with different priorities, 3 cases are identified:
    Case 1: high priority (HP) configured grant PUSCH (CG) vs low priority (LP) dynamic grant PUSCH (DG);
    Case 2: HP DG vs LP CG;
    Case 3: HP CG vs LP CG.
  Rel-16 has specified many new features under URLLC:
    PUSCH repetition type B;
    SRs with different priorities
    PUCCHs with different priorities for HARQ feedback

## Slide 3
Timeline conditions for DG overriding CG in Rel-15
The following can be found in Clause 6.1 in TS 38.214 (Rel-15); they are referred as Rel-15 timeline conditions.

## Slide 4
How to achieve a low scheduling delay?
Assume the Rel-15 timeline conditions (see the previous slide)
  (1) at least N2 symbols before the scheduling PDCCH for DG and the start of the overridden CG transmission occasion/repetition,
  (2) the HARQ ID condition
then if the HP DG is scheduled to start on symbol 0, as the gap between the scheduling DCI for DG and the DG itself is at least N2, the Rel-15 timeline conditions are met, it is allowed.
If the HP DG is scheduled to start on symbol 1 or later, then depending when the its scheduling PDCCH is sent, the Rel-15 timeline conditions may or may not be met. Then scheduling delay due to not supporting cancellation & replacement is at most L-1 symbols (i.e. the HP DG starts on the symbol overlapping with the last symbol of the CG transmission occasion.
  L is the duration of the CG transmission occasion.
Transmission scheme 1
With L OFDM symbols

## Slide 5
Using PUSCH repetition type B and per-repetition overriding
If the LP channel is transmitted with PUSCH repetition type B, as shown above,
let the duration of each repetition be L/K symbols, L is the same as in transmission scheme 1 as shown in the previous slide,
K repetitions are used;
the MCS level of the transmission scheme can be chosen so the transport block size is roughly the same as the transmission scheme 1 (e.g. MCS-Y is higher than MCS-X).
  Then for all practical purposes, two transmission schemes achieve the same, but with the benefit below:
    Note as per-repetition overriding by the HP channel over the LP channel can be performed, the scheduling delay due to not supporting cancellation & replacement is at most L/K-1 symbols. Note the Rel-15 timeline conditions is checked and enforced over DG and the first overridden CG repetition.
Observation 1: by using PUSH repetition type B and per-repetition overriding, the scheduling delay is most L/K-1 symbols.
Transmission scheme 2
PUSCH repetition Type B
With L/K OFDM symbols for each repetition;
K repetitions in total

## Slide 6
Further considerations
The characteristics of the use cases for cancellation and replacement
  The HP uplink traffic has to be latency-sensitive and also its arrival and/or size has to be also unpredictable to build the case for using cancellation and replacement (if the traffic is predictable, then the gNB does not need to resort to cancel & replace); then the UE data buffer status has to be reflected with little latency to the gNB.
  No matter whether information concerning data buffer status is carried by SR and/or BSR, which suggests SR/BSR transmissions has to be frequent, e.g. at several occasions well separated in a slot. With well separated resources taken by SR and/or PUSCH carrying BSR and/or HARQ feedback, essentially the uplink resources are segmented; then it is infeasible to give a LP PUSCH a single long duration.
    Observation 2: any single transmission duration of LP CG (actual transmission) is unlikely to be long. Even with transmission scheme 1, the scheduling latency can be low practice already.
  Other considerations on system operation:
    The overhead due to HARQ ACK feedback, SR and SRS should be considered also; if we budget 4~5 symbols for SR/SRS/HARQ feedback, L in transmission scheme 1 is about 9 symbols.
  Conclusion 1: considering overhead alone, L is likely to be upper-bounded by 9; considering segmentation due to SR/HARQ/SRS, L is likely to be less than 7.
  Observation 3: With transmission scheme 2, if K=3, then the scheduling delay due to not enabling cancellation and replacement with transmission scheme 2 is at most 9/3-1 or 7/3-1 symbols, no larger than 2 symbols.
  Even when Rel-16 PDCCH monitoring with (2,2) is configured, the PDCCH alignment latency alone is 2 symbols; if (4,3) is configured, then the PDCCH alignment latency is 4 symbols; which is present even with cancellation & replacement, which puts any potential benefit with cancellation and replacement in perspective.
    From that, supporting cancellation and replacement does not provide benefit over what is already available in Rel-16, e.g. PUSCH repetition type B with per-repetition overriding.

## Slide 7
Conclusion
Supporting per-repetition overriding with PUSCH repetition type B achieves a small scheduling latency; cancellation and replacement is not well motivated.