## Slide 1: Highlights from RAN#97-e
RAN1 Chair
R1-2208322

## Slide 2: LTE and NR CRs
All RAN1 endorsed LTE CRs submitted to RAN#97-e were approved
All RAN1 endorsed NR CRs submitted to RAN#97-e were approved
  Additionally, one company CR in RP-222609 was approved for frequency hopping pattern for PUSCH with DMRS bundling

## Slide 3: RAN/RAN WG Meeting Planning
Plan in RP-222604 was endorsed

## Slide 4: RAN1 Related Outcomes – Rel-17
Rel-17 NR coverage enhancement
  Support of DMRS bundling in case of UL operation over multiple carriers
    On the issue of supporting DMRS bundling in case of UL operation over multiple carriers, WGs are to continue with their work to resolve the issue (for radio configurations included in R4-2211225) before RAN#98 under the assumption of no RAN1 specification change.
  Frequency hopping pattern for PUSCH with DMRS bundling is determined by ONLY the physical slot index and is independent from system frame number (SFN).
    Company CR in RP-222609 is approved
  Determination of frequency hopping pattern for PUSCH with DMRS bundling
    Regarding UE behavior of restarting DMRS bundling, continue discussions in RAN1

## Slide 5: RAN1 Related Outcomes – Rel-18 (1/3)
Rel-18 Study on expanded and improved NR positioning
  Agreement 1: Defer checkpoint on unlicensed spectrum to RAN#98 (to be reflected in minor update to SID). No work on SL positioning in unlicensed spectrum is expected in the WGs prior to RAN#98.
  Agreement 2: Do not exclude FR2 from the SL positioning study at RAN#97 (no change to SID required)
Rel-18 Network controlled repeaters
  New WID approved in RP-222667
Rel-18 Study on low-power wake-up signal and receiver for NR
  Conclusion: The Rel-18 study on low-power WUS/WUR is for NR only and LTE NB IoT/MTC is not in scope of the SI, no need for a SID update for this
Rel-18 Enhanced support of reduced capability NR device
  New WID approved in RP-222675

## Slide 6: RAN1 Related Outcomes – Rel-18 (2/3)
Rel-18 Multicarrier Enhancement (revised WID RP-222251)
  Clarify in revised WID RP-222251 that the number of TAGs is limited to up to 2 for both 2 bands switching and more than 2 bands switching cases.
    For the work on UL Tx switching with 2 TAGs, RAN1/2 discussion can be triggered by RAN4 LS. No RAN1 spec impact is expected.
  Deprioritize any optimization for unlicensed spectrum operation for designing the multi-cell PUSCH/PDSCH scheduling in Rel-18
  Enhanced Type-2 HARQ-ACK codebook is not supported for the multi-cell PUSCH/PDSCH scheduling in Rel-18.
  Type-1 HARQ-ACK codebook is supported only for the case where co-scheduled cells by a DCI format 1_X have same SCS/carrier type/duplex mode in Rel-18. Additional restriction(s) can be discussed in RAN1
  Configuring more than one scheduling cell for DCI format 0_X/1_X for each scheduled cell is not supported for the multi-cell PUSCH/PDSCH scheduling in Rel-18.
  Following aspects are excluded from multi-cell PDSCH/PUSCH scheduling in Rel-18:
    SCell schedules multiple cells including P(S)Cell
    Different SCS among co-scheduled cells
    Different carrier type (licensed or unlicensed, FR1 or FR2-1 or FR2-2) among co-scheduled cells
    Configuration of both multi-cell PDSCH/PUSCH scheduling and multi-TRP for a scheduled cell
    Support for any sidelink scheduling
    PCell schedules multiple cells by DCI format 0_X/1_X when a sSCell is configured to schedule PCell

## Slide 7: RAN1 Related Outcomes – Rel-18 (3/3)
Rel-18 Sidelink Evolution
  For the Co-Ex objective, RAN1 continues the work on dynamic resource pool sharing based on existing agreements and WID with high priority for Type A devices and operating combination A.
  Start the FR2 objective from RAN#97-e and focus only on updating evaluation methodology in 4Q 2022. Determine in RAN#98-e, whether to continue the study or study+specification work for FR2 until the end of R18.
  For the CA objective, continue to put on-hold and determine whether it can be started in RAN#98-e.
Rel-18 NR NTN enhancements
  Revised WID approved in RP-222654
  The detailed objectives for coverage enhancement:
    To specify PUCCH enhancements for Msg4 HARQ-ACK (e.g. repetition) [RAN1, RAN4]
    To study DMRS bundling for PUSCH taking into account NTN-specifics (e.g. time-frequency pre-compensation) and, if necessary, specify enhancements to the Rel-17 procedures [RAN1]

## Slide 8: BWP Operation without Restriction (provided for information)
The following was endorsed
  No new solution for FG 6-1a shall be added to Rel-17
  If CSI-RS based RLM/BM/BFD are supported by a UE, FG6-1a can work without any issue. FG1-7 (CSI-RS based RLM) and FG 2-24 (SSB/CSI-RS for beam measurement) are mandatory with capability signalling features.
  No change to TU allocation for current RAN4 work in Q4 2022.
  RAN asks RAN4 to do a high level analysis of the options (copied below) in RAN4’s answer to Q2 in RP-221911 and report it to RAN#98 for RAN decision. Options from RP-221911:
    Perform BM/RLM/BFD based on CSI-RS within active BWP
    Perform BM/RLM/BFD based on SSB outside active BWP
      UE’s capability to operate using larger BW covering SSB outside active BWP, or a UE that is equipped with a separate RF chain
      BM/RLM/BFD on SSB outside BWP are performed with shared MG or NCSG for L3 measurement, or dedicated MG or NCSG for RLM/BFD/BM measurements.
    NCD-SSB approach which would work with existing UE hardware architectures (FG6-1) and be compatible with existing RAN4 specifications for BM/RLM/BFD

## Slide 9: Other Information
Rel-17 ASN.1 freeze
  No currently remaining Open Issue for which ASN.1 NBC change is foreseen.
  Recommend that September TS version shall be regarded the Rel-17 baseline.
New Rel-18 study item
  RP-222685: Study on Ambient IoT (RAN-led)

## Slide 10: Rel-18 WID/SID Updates
Relevant to RAN1 objective
  RP-221938: NR sidelink evolution (see slide 7)
  RP-222654: NR NTN (Non-Terrestrial Networks) enhancements (see slide 7)
  RP-222616: Study on expanded and improved NR positioning (see slide 5)
  RP-222675: Enhanced support of reduced capability NR device (New WID)
  RP-222673: NR network-controlled repeaters (New WID)
  RP-222251: Multi-carrier enhancements for NR (see slide 6)
Relevant to other WGs or miscellaneous updates (unique identifier, WI/SI acronym, rapporteur, supporting companies, …)
  RP-222332: Further NR mobility enhancements
  RP-222644: Study on low-power wake-up signal and receiver for NR
  RP-222110: Study on evolution of NR duplex operation