## Slide 1: Highlights from RAN#109
RAN1 Chair
R1-2506701

## Slide 2: LTE and NR CRs / TRs / TSs
All RAN1 endorsed CRs submitted to RAN#109 were approved

## Slide 3: 6GR SID update
RP-252912, SID update from RP-251881 for “Study on 6G Radio”
  Update was made mainly for capturing the workplan for the discussion of migration options

## Slide 4: Update Rel-20 WI/SI for NR with RAN1 impact
SID update from RP-251884 to RP-252964 for adding new objective as below,

## Slide 5: Update R20 RAN1-led SID/WID without adding RAN1 impact
RP-252445, WID update from RP-251870 for “AI/ML for NR air interface Phase 2”
RP-252936, WID update from RP-251856 for “NR MIMO Phase 6”
RP-252894, WID update from RP-251885 for “Solutions for Ambient IoT (Internet of Things) in NR Phase 2”
  Additional RAN2 related change, triggered by RP-252059
RP-252819, SID update from RP-251881 for “Study on Integrated Sensing And Communication (ISAC) for NR”
RP-252824, WID update from RP-251862 for “Coverage enhancements for NR Phase 3”
RP-251933, SID update from RP-251863 for “Study on GNSS (Global Navigation Satellite System)”

## Slide 6: Update Rel-19 WI/SI for NR for regular management
RP-252930 Revised WID: Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface
RP-252332 Revised WID on enhancements of network energy savings for NR
RP-252564 Revised WID Multi-carrier enhancements for NR Phase 3
RP-252105 Revised WID: Solutions for Ambient IoT (Internet of Things) in NR

## Slide 7: RAN1 involved LS
RP-251919 Reply LS to R2-2503169 on signalling feasibility of dataset and parameter sharing (S2-2508104; to: RAN2; cc: RAN, RAN1, RAN3, SA, SA3, SA5)
  No RAN1 action is needed
RP-251920 Reply LS to R2-2503169 on signalling feasibility of dataset and parameter sharing (S5-254083; to: RAN2; cc: RAN, SA, RAN1, RAN3, SA2, SA3)
  No RAN1 action is needed

## Slide 8: New Rel-20 WI/SI for NR with potential RAN1 impact
WID RP-252962 was approved for “Enhanced requirements for NR NTN and IoT NTN Phase 2”
  Whether potential RAN1 impact is doable is to be decided by June, 2026.

## Slide 9: RAN-level 6G study (1/3）
The RAN-level study covering 6G scenarios/use cases and requirements progressed with endorsed pCR for TR 38.914:
  RP-252888, pCR for 38.914 on Deployment scenarios for 6G
  RP-252947, pCR for 38.914 on Key performance indicators for 6G
  RP-252870, pCR for 38.914 on Requirements for architecture and migration for 6G
  RP-252960, pCR for 38.914 on Requirements of new and existing services for 6G
  RP-252951, pCR for 38.914 on spectrum utilization requirements
RP-252882, TR 38.914 v0.2.0 for Study on 6G Scenarios and requirements

## Slide 10: RAN-level 6G study (2/3, agreements not captured in pCR）
Following points were endorsed in RP-252883 in RAN#109
  For 3GPP internal evaluation, define energy efficiency as a quantitative KPI in 3GPP for both network and device
  For 3GPP internal evaluation, at least empty load and partial load cases should be evaluated in 6GR study
    Evaluate via system level simulation (SLS)
    Other evaluation methods are not precluded when relevant
  For 3GPP internal evaluation, UE/Network power model is to be discussed in RAN1
  For 3GPP internal evaluation, link budget is used as the evaluation methodology for coverage when applicable
  For 3GPP internal evaluation, the target for coverage is to be determined by RAN
    FFS: Exact coverage target value(s)
    FFS: Additional details considering control/data channel
    Following points were endorsed in RP-252943 in RAN#109
  For 6G Massive Communication (IoT), the minimum number of UE receive/transmit antenna is 1 for lowest-tier device
    Reflect this agreement in the device type section of the TR
  6GR should study the sensing modes, including TRP monostatic, TRP-TRP bistatic, TRP-UE DL, UE-TRP UL, UE-UE bistatic and UE monostatic

## Slide 11: RAN-level 6G study (3/3, agreements not captured in pCR）
  Slides 3 and 4 were endorsed in RP-252943 in RAN#109
    Side 3
    For 6GR deployment scenarios focus on the following,
      analyze that the air interface design (aka “6GR”) to be developed during the 6G Radio Study fulfills the requirements of IMT-2030 (for the ITU process)
      analyze the performance of “6GR” in realistic/practical deployment scenarios and where applicable, allow comparison to 5G-Advanced
    Include carrier frequency of 15 GHz for the 6G scenarios (other than rural scenario) as part of 6G study.
    Note: Carrier frequency of 15GHz has not been confirmed by ITU-R/WRC
    Slide 4

## Slide 12: Diverse UE types – 1/3
3 proposals were endorsed and captured in the conclusion part of RP-252873
  It was confirmed that RAN1 will continue to study both the minimum spectrum allocation and the smallest maximum UE bandwidth. However, it is hard to purely discuss these two elements in RAN1.
Chair guidance
  RAN1 will focus on how to support the minimum spectrum allocation, especially the case where the minimum spectrum and the smallest maximum UE bandwidth can’t match, considering that it is hard to purely discuss these two elements in RAN1

## Slide 13: Diverse UE types – 2/3
This part will be discussed in RANP, and RAN1 will not have schedule for it in next quarter.

## Slide 14: Diverse UE types – 3/3
In RAN1, no intention to set dedicated schedule / agenda for discussion of the individual attributes / parameters / factors for the purpose of defining device types
  The individual attribute / parameter / factor will be discussed in the most appropriate available agendas of each RAN1 meeting.
As to how to associate this attributes / parameters / factors with device types will be left to RANP

## Slide 15: Numerology and Spectrum for 6GR
Given the discussion in RAN#109 and the agreement captured in RP-252963 shown at the right side,
  RAN1 will suspend the discussion on second numerology for FDD frequency, i.e., RAN1 will not discuss the two “FFS” of “for sub 6GHz” in Q4, 2025.
  RAN1 will continue to resolve the part of “FFS: for around 15GHz”

## Slide 16: Management of TEI
RP-252060 Review of TEI before RAN#109
  Driven by the following observations,
    Observation 1: Compared to RAN#104, a large number of TEI identifiers have been associated with many TEI CRs. More than 10 CRs is for one TEI identifier is definitely not small, and even 6-9 CRs is not a small amount. This is a significant deterioration of the situation at RAN#104 where only one TEI identifier had 7 CRs compared to RAN#100.
    Observation 2: A large number of TEI violates the rule that all work shall complete in all WGs within one cycle - and another (general) rule that all CRs shall be brought together as a package
  2 proposals of this contribution were endorsed.
    Proposal 1: TSG RAN shall remind WG leadership and delegates that proper Work Items need to be defined for work that requires multiple CRs already in the first cycle, and shall police it as too many TEI identifiers are used for work that is clearly too big to be considered TEI.
    Proposal 2: Proponents of TEI CRs shall explicitly check during the quarter that all relevant work is completed in all RAN WGs before asking approval from RAN plenary and RAN (TSG/WG) leadership shall police this.

## Slide 17: RAN1 TU Allocation
Rel-20 RAN1 WI/SI | 2025.Q3 | 2025.Q4 |  | 2026.Q1 | 2026.Q2 |  | 2026.Q3 | 2026.Q4 |  | 2027.Q1
 | RP#109 | RP#110 |  | RP#111 | RP#112 |  | RP#113 | RP#114 |  | RP#115
 | R1#122 | R1#122b | R1#123 | R1#124 | R1#124b | R1#125 | R1#126 | R1#126b | R1#127 | R1#128
Nominal TUs for maintenance | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 
Additional TUs for maintenance | 8 | 4 | 4 | 2 | 0 | 0 | 0 | 0 | 0 | 
Misc. impact from other WGs |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
Reserved TUs | 2.5 | 3 | 3 | 2.5 | 3 | 3 | 2 | 2 | 2 | 
Rel-20 TEI |  |  |  |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 
AI/ML Air Interface | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 
A-IoT (Study Item) | 3.5 | 3.5 | 3.5 | 3.5 |  |  |  |  |  | 
A-IoT (Work Item) |  |  |  |  | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 
NR-MIMO | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
Coverage Enh |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |  |  |  | 
ISAC (Study Item) | 1 | 1 | 1 | 1 |  |  |  |  |  | 
NR-NTN GNSS resilient (SI, WI – TBD) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
IoT-NTN (RAN2-led) |  |  |  | 0.5 | 0.5 | 0.5 |  |  |  | 
6G study | 8 | 10 | 10 | 12 | 14 | 14 | 16 | 16 | 16 | 16
Total RAN1 TUs | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 
NR-NTN GNSS resilient: TUs for 2026.Q3 and 2026.Q4 are pre-allocated for a possible WI depending on the outcome of study item and decision in RAN#112