## Slide 1: Remaining issues on AI11.1 - overview of 6GR air interface
Moderator (NTT DOCOMO)

## Slide 2: Scalable 6GR design
Proposal 3.1b:
For scalable 6GR design for diverse device types, RAN1 to consider
  Striving for functionality designs that can be commonly applied to all 6G device types
The functionalities commonly applicable to all 6G device types include, but not limited to
  Basic PHY features, such as waveform, coding, frame structure, single numerology per band
  Idle mode procedures
  Initial access procedures
  DL/UL control
  Basic scheduling/HARQ
  MRSS
  Coverage enhancements
  Energy saving

## Slide 3: Smallest maximum supported UE BW
Proposal 4.1b:
For the smallest maximum supported RF and BB UE BW without spectrum aggregation for at least one low-tier device type supported by 6GR framework, from physical layer perspective, RAN1 to consider at least
  Device complexity
  Overall system performance impact
  Energy efficiency for both BS and UE
  Minimum spectrum allocation
  Aim at a single common signals/channels design in idle mode and initial access, targeting scalable and forward compatible design for diverse device types, as well as meeting mobile broadband service requirements as high priority

## Slide 4: Minimum spectrum allocation
Proposal 4.2b:
RAN1 to consider following to operate 6GR on the minimum spectrum allocation
  Opt1: common signals/channels BW for initial access are punctured to fit into the minimum spectrum allocation, if the minimum spectrum allocation is smaller than the common signals/channels BW for initial access (if this case is supported)
  Opt2: Separate design of the common signals/channels for initial access for the minimum spectrum allocation from other spectrum allocations , if the minimum spectrum allocation is smaller than the common signals/channels BW for initial access for other spectrum allocations
  Opt3: A single design of the common signals/channels for initial access which is applicable to any spectrum allocations

## Slide 5: MRSS
Proposal 6.2b:
High-level aspects to consider for NR-6GR MRSS include, but not limited to
  UE/NW implementation complexity
  Resource allocation coordination between NR-6GR
  Reliance on specific NR UE features
Note: Focus on typical NR deployments (NW and UE)
  Traffic pattern
  Radio resource utilization
  Signalling overhead
  Operating bands/carriers
  NR and 6GR TRP co-location
  NW Energy efficiency
  Numerology impact/alignment
  Frame/slot/symbol boundary impact/alignment
  RB boundary impact/alignment

## Slide 6: SS structure
Proposal 7.1b:
High-level aspects which impact on the 6GR sync signal structure include, but not limited to
  Reduced number of sync raster
  Support of all 6G devices
  Support of minimum spectrum allocation
  Detection/tracking performance, latency, and complexity
  Coverage target
  Scalability to operate on the supported deployments and spectrum, including multi-beam/TRP operation
  Note: Aspects impacting on the periodicity is to be discussed under AI11.5

## Slide 7: BWP framework
Proposed observation 8.1b:
The lessons learned from NR BWP framework include, but not limited to
  A lot of potential uses, including adaptation to traffic demands and energy savings
  A lot of RRC parameters under BWP configuration
    results in unnecessarily large overhead and unnecessary RRC parameter options
  BWP switching delay
    too large due to the assumption that all RF/BB parameters of new BWP are re-loaded at UE sides
  SCS switching
    complicated but less motivated.
  Excessive BWP types
    including BWP types that have not been effectively used in practical NW, e.g., default BWP, dormant BWP.
  Center frequency of DL/UL BWP in TDD
    limits the operational flexibility
  lack of early RAN4 involvement
    leading to large MPR/A-MPR
  Inherent restrictions
    When a BWP is not covering the sync signal bandwidth, it can lead to different approaches for maintaining sync
  Bandwidth of DL/UL BWP
    unnecessarily contiguous bandwidth

## Slide 8: Spectrum utilization and aggregation
Proposed observation 9.1b:
The lessons learned from NR spectrum utilization and aggregation framework include, but not limited to
  CA has been a beneficial feature in LTE and NR
  Pcell vs Scell
    Allowing some functionalities only on specific cell like PCell may limit resource utilizations
  Coupling DL and UL carriers for a cell
    inefficient and ineffective due to different requirements and limitations between DL and UL
    SUL/SDL, UL Tx switching, SRS carrier switching, LBCA switching operate differently
    SUL scheme is bound to dedicated SUL bands with UL-only resource
    ensuring the presence of a corresponding downlink CC used as a reference for measurements
  UL Tx switching
    did not incorporate all UL transmissions, complicating its use
    mandates UE to support at least N DL CCs and the N DL CCs are activated, which leads to high DL capabilities requirement and high UE power consumption
  SSB adaptation for Scell
    limited applicable scenario for SSB-less SCell operation and On-demand SSB SCell operation
  Activation of additional carrier
    Slow not only because of signaling protocols and RAN4 requirements, but also because of very relaxed CSI accuracy for the newly activated carrier
    faces a dilemma of choosing the high service latency caused by SCell activation and high UE power consumption by keeping SCell always activated
    SCell dormancy is impractical as this feature is defined on top of BWP framework, which is unnecessarily flexible and complicated.
  Features (such as HARQ) defined per carrier
    prevents further improvements on user throughput and latency via cross-carrier operation
    inefficient and ineffective for better spectrum utilization, load balancing, NW/UE energy saving
  The maximum number of bands in NR multi-band operations
    actually limited by the maximum UE RF+BB hardware capacity in commercial networks
  Concurrent transmissions of UL-CA/EN-DC
    only beneficial for UEs who are close to gNB and have redundant UE Tx power and its symbol-by-symbol UL power control requires very tight coordination between PCell gNB and SCell gNBs.
    need to require a semi-static UL power split for the UE in absence of gNB scheduler coordination.
    Only supported for connected mode
  Fragmented spectrum
    not efficiently utilized and latency is unnecessarily increased under NR CA framework
    high cell management overhead
  Signalling overhead and UE processing complexity of PHY channels
    scale with the number of aggregated carriers rather than the aggregated bandwidth size
  Cross-carrier scheduling
    Complex capability splitting of UE for one scheduled cell being scheduled by multiple scheduling cells

## Slide 9: NTN
Proposal 10.2a:
The technical aspects affected by NTN characteristics include, but not limited to
  Initial access, including cell search and SSB periodicity
  GNSS-less/resilient operation
  Coverage enhancements
  Positioning
  NTN-TN and NTN-NTN mobility
  Spectrum utilization and aggregation framework
  Capacity
  Large propagation delay
  Large doppler shift/drift and timing drifting
  Duplexing
  Beamforming / beam management
  TN-NTN in the same spectrum
  6G NTN coexistence with IoT-NTN or NR-NTN in same beam
  satellite moving

## Slide 10: OPEX/CAPEX
Proposal 11.2:
Study how to address the following RAN requirement in 6GR physical layer design, considering, e.g., complexity reduction, energy efficiency, market fragmentation, MRSS migration aspects
  The design of the 6G RAN shall enable lower CAPEX/OPEX with respect to current networks.