## Slide 1: Remaining issues on AI11.1 - overview of 6GR air interface
Moderator (NTT DOCOMO)

## Slide 2: Scalable 6GR design
Proposal 3.1b:
For scalable 6GR design for diverse device types, RAN1 to consider
  Striving for functionality designs that can be commonly applied to all 6G device types
The functionalities commonly applicable to all 6G device types include, but not limited to
  Basic PHY features, such as waveform, coding, frame structure, single numerology per band
  Basic idle mode procedures from RAN1 perspective
  Basic initial access procedures
  Basic DL/UL control, scheduling/HARQ
  MRSS
  [Coverage enhancements]
  [Energy saving]
  Note: adjustment on the design is allowed for a certain device type

## Slide 3: Smallest maximum supported UE BW
Proposal 4.1b:
For the smallest maximum supported RF and BB UE BW without spectrum aggregation for at least one low-tier device type supported by 6GR framework, from physical layer perspective, RAN1 to consider at least
  Overall device complexity
    Note: also taking into account other complexity reduction techniques than BW reduction
  Overall system performance impact
  Energy efficiency for both BS and UE
  Minimum spectrum allocation
  Aim at a single common signals/channels design in idle mode and initial access for diverse device types, as well as meeting mobile broadband service requirements as high priority
  Note: other aspects (e.g. economies of scale) can be considered by TSG RAN when they make decision on the BW

## Slide 4: Minimum spectrum allocation
Proposal 4.2b:
RAN1 to consider following to operate 6GR on the minimum spectrum allocation
  Opt1: common signals/channels BW for initial access are punctured to fit into the minimum spectrum allocation, if the minimum spectrum allocation is smaller than the common signals/channels BW for initial access (if this case is supported)
  Opt2: Scalable design of the common signals/channels for initial access for the minimum spectrum allocation from other spectrum allocations , if the minimum spectrum allocation is smaller than the common signals/channels BW for initial access for other spectrum allocations
  Opt3: A single design of the common signals/channels for initial access which is applicable to any spectrum allocations

## Slide 5: MRSS
Proposal 6.2b:
High-level aspects to consider for NR-6GR MRSS include, but not limited to
  UE/NW implementation complexity
  Resource allocation coordination between NR-6GR
    Including whether NR and 6GR TRP are always co-located or not
  Radio resource utilization
  Signalling overhead
  Operating bands at least existing FR1
  Alignment in time/frequency resource (e.g., numerology, RB, slot, symbol, UL/DL direction in TDD operation)
  Reliance on availability of specific NR functionalities
Note: Focus on existing NR deployments (NW and UE)

## Slide 6: SS structure
Proposal 7.1b:
High-level aspects to consider for the 6GR sync signal structure include, but not limited to
  Sync raster design
  Spectrum allocation
  smallest maximum supported RF and BB UE BW without spectrum aggregation
  mobile broadband service requirements as high priority
  Energy efficiency for both BS and UE
  Detection/tracking performance, latency, and complexity
    Including initial cell search
  Coverage target
  Common design for diverse device types
  Consideration of the supported deployment and spectrum
  Consideration on whether the same sync signal is to be used (or not) for all procedures
  Note: Aspects impacting on the periodicity is to be discussed under AI11.5

## Slide 7: BWP framework
Proposed observation 8.1c:
The lessons learned from NR BWP framework include, but not limited to
  excessive BWP-specific BB/RF configuration parameters, which leads to UE long BWP switch latency
  SCS switching under BWP framework is complicated
  Some scenarios (e.g. non-overlapped BWPs) where DCI-based BWP switching can have reliability issue
  lack of early RAN4 involvement, which caused sub-optimal design

## Slide 8: Spectrum utilization and aggregation
Proposed observation 9.1b:
The lessons learned from NR spectrum utilization and aggregation framework include, but not limited to
  CA has been a beneficial feature in previous generations
  Not all functionalities are available from initial release
  Operating scenarios of CA and DC have some overlap
  Some functionalities are supported only on Pcell
  Slow and complex activation of additional carrier
  Inefficiency from coupling DL and UL carriers for a cell
  Utilizing fragmented spectrum is not considered well
  Features (such as HARQ) defined per carrier leads to sub-optimal performance
  Signalling/configuration overhead and UE processing complexity of PHY channels due to per CC constraint
  limited applicable scenario of SSB adaptation for Scell
  Late introduction of UL TX switching leads to restricted applicability/performance

## Slide 9: NTN
Proposal 10.2a:
The aspects to consider for supporting NTN include, but not limited to
  Initial access, including cell search and SSB periodicity
  Coverage
  Duplexing
  Capacity
  Signalling overhead
  GNSS-less/resilient/based operation
    Note: considering Rel-20 5G-A discussion
  Large/varying doppler and propagation delay
  Beamforming / beam management / beam hopping

## Slide 10: OPEX/CAPEX
Proposal 11.2a:
High-level aspects to consider to enable lower CAPEX/OPEX with respect to current networks include, but not limited to
  UE/NW implementation complexity
  UE/NW Energy efficiency
  MRSS
  Migration
  Spectrum efficiency