## Slide 1: WF on Synchronized New Carrier
Intel Corporation, CMCC, Ericsson, ST-Ericsson, CATR, Texas Instruments, CATT, Mediatek, Nokia Siemens Networks, Nokia, Renesas Mobile Europe Ltd, Interdigital, NEC, Qualcomm Inc., Samsung, HTC, China Telecom, Research In Motion, Kyocera, Broadcom
3GPP TSG RAN WG1 Meeting #72
St. Julian’s, Malta, January 28th – February 1st, 2012
R1-130709
Agenda: 7.3.1.3
Document for: Decision

## Slide 2: Backgrounds (1/2)
Agreements in RAN1#68bis (at least for the unsynchronized case)
  Rel-8 PSS/SSS sequences are transmitted.
  New carrier type can carry 1 RS port (consisting of the Rel-8 CRS Port 0 REs per PRB and Rel-8 sequence) within 1 subframe with 5ms periodicity
    This RS port is not used for demodulation

## Slide 3: Backgrounds (2/2)
Scenarios for synchronized new carrier
  Would be limited to the case e.g. intra-band contiguous carrier aggregation using a single RF front end
  Not the typical scenario for stand alone new carrier as well as for small cell enhancement in Rel-12
Possibility of removing PSS/SSS/CRS
  CRS might need to be transmitted for the purpose of RRM measurement for NCT regardless of time/frequency tracking (pending from RAN4 response).
  PSS/SSS may be removed but overhead saving seems not significant
    For example, potential overhead reduction in FDD would be 2.87/1.14/0.69/0.34/0.23/0.17% for 1.4/3/5/10/15/20MHz.
    Similar view for the removal of the reduced CRS

## Slide 4: Proposal
The same design as in non-synchronized carrier is applied for synchronized new carrier.