## Slide 1: WF on Introduction of Elevation Domain Parameters in 3D Channel Modeling
Nokia Siemens Networks, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Anite Telecoms Ltd, Broadcom, CATT, CMCC, Elektrobit, ETRI, HiSilicon, Huawei, Intel Corporation, InterDigital, KDDI, LG Electronics, Motorola Mobility, NEC, New Postcom, Nokia, NTT DOCOMO, Orange, Qualcomm , Samsung
3GPP TSG RAN WG1 #73
Fukuoka, Japan, 20th-24th May 2013
Agenda Item: 6.2.6.2
R1-132748

## Slide 2: Proposal
The 3D channel modeling will be based on current ITU channel models
  Reuse the ITU channel coefficient generation procedure ( Figure 4.1 in WINNER II, D 1.1.2 V1.2)
:
:
:
Coefficient generation
Small scale parameter
General parameters
Set scenario,
network
layout and antenna
parameters
Assign propagation
condition
(NLOS/LOS)
Calculate path loss
Generate correlated
large scale paramters
(DS, AS, SF, K)
Generate delays
Generate cluster
powers
Generate arrival and
departure angles
Perform random
coupling of rays
Draw random initial
phases
Generate channel
coefficient
Apply path loss
shadowing
Generate XPRs
1
2
3
4
9
8
7
6
5
10
11
12

## Slide 3: Proposal: Overview of each step
Step 1: Set environment, network layout, and antenna array parameters
  Choose scenario from
    3D UMa
    3D UMi
Step 2: Assign propagation condition (LOS/NLOS)
Step 3: Calculate path loss
Step 4: Generate correlated large scale parameters, i.e. delay spread, angular spreads, Ricean K factor and shadow fading term
Step 5: Generate delays
Step 6: Generate cluster powers
Step 7: Generate arrival angles and departure angles
  Both azimuth and elevation
Step 8: Coupling of rays within clusters
  Both azimuth and elevation
Step 9: Generate XPRs
Step 10: Draw random initial phases
Step 11: Generate channel coefficients
Step 12: Apply pathloss and shadowing

## Slide 4: Proposal
At least the following six parameters will be added in 3D channel modeling
  EoA: Elevation angle of arrival
    Includes Median EoA
  EoD: Elevation angle of departure
    Includes Median EoD
  ESA: RMS elevation angle spread of arrival
  ESD: RMS elevation angle spread of departure
  Cluster ESD: cluster elevation angle spread of departure
  Cluster ESA: cluster elevation angle spread of arrival
Identify necessary modification of each step due to the introduction of the above parameters, e.g.
  Step 4 will be impacted by ESA/ESD
  Step 7, 8 and 11 will be impacted by EoA/EoD