## Slide 1: Way Forward for Small Cell On/Off
Huawei, HiSilicon, Panasonic, Samsung
3GPP TSG RAN WG1 Meeting #73 R1-132778
Fukuoka, Japan, May 20-24, 2013
Agenda item: 6.2.5.2.1

## Slide 2: Performance Observations
Significant UPT benefits are observed at least when dynamic (i.e., subframe-level) small cell on/off is assumed and with low/medium load
  Gains are also observed when semi-static adaptation is assumed
  FFS performance benefits with feasible time scale
Potential impacts on other system performance
  Coverage/idle UE support: rely on coverage layer/cell
  Mobility: FFS (related to RAN2 Het-Net mobility study and RAN2 small cell study)
  Energy consumption: reduction of energy consumption is expected

## Slide 3: Feasible Time Scales
Baseline value of the feasible time scale to be used for further evaluation of network adaptation, if using currently existing procedures, is as following:
  Time before a UE can use a just turned on small cell: [400] ms
  Time before a new arrived UE (as in FTP 1) can use an already on small cell: [200] ms
For faster time scale (e.g., subframe-level), companies need to show the performance along with the feasible procedure(s) (e.g., dual connectivity) to handle the following aspects:
  Cell detection/configuration and attachment
  Time/frequency synchronization
  CSI/RRM measurement and report
  Legacy user handling
Capture typical example of event/time diagram(s) or table(s) of these techniques in the TR

## Slide 4: Alignment of Assumptions
Parameters | Values | Note
Scenario | Scenario 2a | 
Schemes | 1. Semi-static on/off 2. On/off with feasible time scale 3. Dynamic on/off | Baseline is no small cell on/off
Time scale | See page 3 | 
Traffic load | Low: average RU around 15% Medium: average RU around 40% | 
Traffic model | Scheme 1: FTP 3 with 30 UEs Scheme 2: FTP 1 Scheme 3: FTP 1 or FTP 3 with 30 UEs | 
Cluster configuration | 1 cluster of 10 small cells | 
CRS overhead | 2 CRS ports | 
Number of MBSFN subframes configured | 0 and 6 | 
Cell association | RSRQ + bias with realistic buffer Bias of 0 dB as baseline | Not to limit cell association study

## Slide 5: Supporting Mechanisms
Further study the following mechanisms:
  UL/DL signal and measurement enhancements for network adaptation decision making
  Enhancements for cell association and load balancing/shifting
  Signaling (e.g. RRC) to inform UE the network adaptation
  Mechanisms to cope with or avoid disruptive interference/measurement jumps due to network adaptation
  Backhaul signaling and coordination enhancements