## Slide 1: WF on D2D PUSCH Transmission
Qualcomm, General Dynamics Broadband, ITRI, Samsung
3GPP TSG RAN WG1 #75 R1-135934 San Francisco, US
November 11th – 15th, 2013

## Slide 2: D2D PUSCH Transmission
For communication following was agreed to
  PUSCH structure is reused for D2D data communication physical channel, including:
    24 bit CRC is inserted
    Turbo coding is used
    Rate matching is used for bit size matching and possibly for generating multiple transmissions.
    Scrambling is to be used for interference randomization.
    PUSCH DMRS is transmitted
      Possible additional RS is FFS
    Possible modifications to interleaver FFS
    CP length FFS
    Detailed RE mapping FFS
    Guard period details FFS

## Slide 3: D2D PUSCH Transmission
For discovery following was agreed to
  PUSCH structure is reused, with:
    CRC is inserted, FFS between 16 and 24 bits
    Channel coding is used, FFS between Rel-8 turbo and tail-biting convolutional codes
    Rate matching is used for bit size matching and possibly for generating multiple transmissions
    Scrambling is to be used for interference randomization
      FFS whether UE-specific or not
    PUSCH DMRS is transmitted
      Possible additional RS is FFS
    Possible modifications to interleaver FFS
    CP length FFS
    Detailed RE mapping FFS
    Guard period details FFS
  FFS: consider the need for a time-varying hashing/scrambling function prior to channel coding

## Slide 4: Proposal
For both communication and discovery
  24 bits CRC is inserted
  Turbo coding is used
  No modification to interleaver
For discovery only
  Scrambling be independent of cell id and UE id
  No time-varying hashing/scrambling function prior to channel coding