## Slide 1: Way Forward on NAICS network signaling/coordination
MediaTek, Blackberry,…
3GPP TSG RAN WG1 Meeting #75
San Francisco, USA, 11th – 15th Nov. 2013
R1-135962

## Slide 2: Observations
Compared to requiring NAICS receivers to detect all interference parameters, some network signalling/coordination can be beneficial for reducing receiver complexity and/or improve performance with increased robustness
  The subset of transmission parameters that can be considered for signalling and that for receiver detection are FFS
  The transmission parameters are listed in the RAN4 agreed receiver assumption section of TR36.866, and generally include:
    Parameters that are higher-layer configured per the current specifications (e.g., TM, cell ID, MBSFN subframes, CRS antenna ports, PA, PB, data-to-CRS power ratio)
    Parameters that are dynamically signalled per the current specifications (e.g., CFI, PMI, RI, MCS, resource allocation, DMRS ports, n^DMRS_ID used in TM10)
    Other deployment related parameters (e.g., synchronization, CP, subframe/slot alignment)
  Some higher-layer configured parameters may be signalled or detected
    Such assistance signaling may use higher layers regardless of whether the associated transmission parameter is higher-layer configured or dynamic
  Some dynamic parameters may be coordinated, but with scheduling constraint, detected or signalled or a combination of the three
  Other deployment related parameters may be coordinated or detected.
  Semi-static coordination signalling or coordination is suited for non-ideal backhaul
  Dynamic coordination may be feasible only under ideal backhaul
    The need of dynamic signalling and its mechanism (e.g., broadcast vs. unicast, from serving or interference cell) still need further study, taking into account the trade-off between gain and signalling overhead.
  Other potential PHY impact needs further study (e.g., CSI feedback)
Proposal : Capture the above observations in the “Specification Impact” section of TR36.866