## Slide 1: Polarized Antenna modelling
3GPP TSG-RAN WG1 #76 R1-140765
Prague, Czech Republic, February 10 – February 14, 2014
Source: Ericsson
Agenda Item: 7.2.7.2
Document for: Discussion & Decision

## Slide 2: Background Angle independent model
Polarized antenna model well-established ever since TR36.814
  Polarization is angle independent according to where is the so-called slant angle (usually ±45◦)
Angle independent model earlier motivated by measurements in R1-092741
  Further motivations in R1-092795
Can be directly realized as a physical antenna
  Obtained by feeding the same signal to an electrical dipole antenna and an electric loop antenna

## Slide 3: Background The dipole polarization model
An alternative polarization model was discussed in RAN1 #75 (c.f. [75-10] on reflector)
Polarization modelled as mechanical rotation of a vertically polarized antenna
Polarization direction changes with the angle
  Example: ±45 cross-pole antennas both get vertically polarized at
Polarization modeled using mechanical rotation of a dipole!

## Slide 4: Measurement On real-life antennas
Measurements conducted on 9 different real-life base station antennas
  Antennas targeting 120 degree sectors
Antennas commonly found in commercial deployments from several well-known antenna vendors
Measurement of phi and theta field components for ±45 polarized antenna pair at horizontal cut
Definition of parallelity
Parallelity is zero for angle independent model
  So the two ±45 polarized antennas have orthogonal polarization regardless of angle

## Slide 5: Measurement results
Dipole model exhibits extreme behavior at angles
Angle independent model shows parallelity very close to most antennas over a wide range of angles
Real-life antennas tend to maintain orthogonal polarization over a wide range of angles
Dipole polarization model far from real-life polarization properties! Well-established angle independent model provides a more accurate approximation of real-life polarization properties!

## Slide 6: Conclusions
Two different polarization antenna models
  Well-established angle independent model
  Dipole based model (mechanical rotation of vertically polarized antenna)
Both models have direct physical counterparts and can hence be realized
Measurements on a multitude of real-life antennas conducted
  Real-life antennas have very different properties from dipole based model
Angle independent model is a better approximation of real-life antenna polarization properties!
(In line with previous measurement results in R1-092741)