## Slide 1: WF on UE processing capability
CMCC, CATT
R1-142641

## Slide 2: Proposal
  Increased processing capability in terms of “Maximum number of DL-SCH transport block bits received within a TTI” (described in R1-142637*) can be used enabled even if 256QAM is not enabled
  Decoupling capability for supporting 256QAM for UE categories 4,5,6,7,9,10
    One capability related to higher processing capability, i.e., Maximum number of DL-SCH transport block bits received within a TTI.
    One capability related to the support of other 256QAM aspects, e.g., requirements on RF of the UE receiver, 256QAM constellation mapping and etc.
* Note: R1-142637 WF on 256QAM UE category handling Ericsson

## Slide 3: Background
Motivation of decoupling capability for supporting 256QAM (taking cat 4 UE as example),
  Alt 1: Decoupling capability (as proposed in slide 2)
 | Maximum number of DL-SCH transport block bits received within a TTI | Maximum number of bits of a DL-SCH transport block received within a TTI | Maximum number of DL-SCH transport block bits received within a TTI
Cat 4 | 150752 (Legacy) | 75376 (64QAM) | 1827072
 | [200000] (New) | [100000] (256QAM) | 
Indicated by
(b) One capability related to the support of other 256QAM aspects, e.g., requirements on RF of the UE receiver, 256QAM constellation mapping and etc.
Indicated by
(a) One capability related to higher processing capability, i.e., Maximum number of DL-SCH transport block bits received within a TTI

## Slide 4: Background
Motivation of decoupling capability for supporting 256QAM(taking cat 4 UE as example) (cont.)
  Alt 2: one capability
 | Maximum number of DL-SCH transport block bits received within a TTI | Maximum number of bits of a DL-SCH transport block received within a TTI | Maximum number of DL-SCH transport block bits received within a TTI
Cat 4 | 150752 (Legacy) | 75376 (64QAM) | 1827072
 | [200000] (New) | [100000] (256QAM) | 
Indication by one capability related to support 256QAM or not

## Slide 5: Background
Example 1 (for cat 4 CA capable UE): 10MHz+10MHz CA migrate to 10MHz+20MHz CA
  The peak data rate of cat 4 UE for each alternative is as follows
  Alt 1 outperforms Alt 2 from 10MHz+10MHz migrate to 10MHz+20MHz for cat 4 UE.
Cat 4 |  | 10MHz+10MHz CA | 10MHz+20MHz CA
256QAM is NOT supported | Alt 1: Decoupling capability | 150Mbps | [200Mbps]
 | Alt 2: one capability | 150Mbps | 150Mbps
The Maximum number of DL-SCH transport block bits received within a TTI is restricted to 150752, thus it leads to the limitation the increase of peak data rate

## Slide 6: Background
Example 2 (for cat 4 CA capable UE): 20MHz migrate to 20MHz+10MHz CA or 20MHz+20MHz CA
  The peak data rate of cat 4 UE for each alternative is as follows
  Alt 1 outperforms Alt 2 from 20MHz migrate to 20MHz+10MHz CA or 20MHz+20MHz CA
Cat 4 |  | 20MHz | 20MHz+10/20MHz CA
256QAM is NOT supported | Alt 1: Decoupling capability | 150Mbps | [200Mbps]
 | Alt 2: one capability | 150Mbps | 150Mbps

## Slide 7: Background
Example 3 (for cat 6/7 4-layer and CA capable UE): 20MHz migrate to 20MHz+10MHz CA or 20MHz+20MHz CA
  The peak data rate of cat 4 UE for each alternative is as follows
  Alt 1 outperforms Alt 2 from 20MHz migrate to 20MHz+10MHz CA or 20MHz+20MHz CA (4-layers)
Cat 6/7 |  | 20MHz | 20MHz+10/20MHz CA
256QAM is NOT supported | Alt 1: Decoupling capability | 300Mbps | [400Mbps]
 | Alt 2: one capability | 300Mbps | 300Mbps