## Slide 1: Summary of initial co-existence evaluations
Huawei, HiSilicon, Cisco, NTT Docomo, ZTE
3GPP TSG RAN WG1 #79
San Francisco, USA, 17th – 21st November 2014
Agenda item 6.3.2.2
R1-145320

## Slide 2: Introduction
Initial coexistence results(*) between LAA and WiFi have been provided by the following sources at RAN1#79:
  [1] Huawei, HiSilicon, R1-144589, “Preliminary results of coexistence evaluation for LAA”.
  [2] NTT DOCOMO, R1-145217, “Initial evaluation results for co-existence performance of LAA with LBT mechanism”.
  [3] Samsung, R1-144738, “Initial evaluation results on LAA”.
  [4] ZTE, R1-145197, “Preliminary performance evaluation for Licensed-Assisted Access using LTE”.
  [5] Cisco Systems, R1-144603, “Initial coexistence evaluations comparing LAA versus Wi-Fi”.
  [6] Broadcom Corporation, CableLabs, R1-145168, “Initial Evaluation of Clear Channel Assessment mechanisms for LAA”.
  [7] CableLabs, Broadcom, R1-145195, User Plane Traffic Duplex Considerations.
(*) [1-6] show throughput results, [7] shows the probability of successful channel access

## Slide 3: Summary of throughput results
6 sources simulated the coexistence of LAA and WiFi (with CCA-ED and CCA-CS), among which 5 sources simulated LAA with LBT based on CCA-ED and 2 sources simulated LAA without LBT.
  2 sources showed that LAA without LBT degrades WiFi more than another WiFi
    1 source with a single carrier, 1 source with 4 carriers
  4 sources showed that LAA with CCA-ED degrades WiFi less than another WiFi
    3 sources with a single carrier, 1 source with 4 carriers
  1 source showed that LAA with CCA-ED degrades WiFi more than another WiFi
    1 source (2 companies) with a single carrier

## Slide 4: Proposal
Proposal for the next steps of the study:
  All coexistence performance evaluations should consider LBT for LAA
    Continue evaluations to assess the coexistence using LBT for LAA based on different CCA mechanisms (considering solutions proposed by companies)

## Slide 5: Appendix

## Slide 6: WiFi with LAA vs. WiFi with another WiFi
Source | Low Load | Mid Load | High Load | Latency
[1] Huawei | ~25% UPT gain | >250% UPT gain | >250% UPT gain | 
[2] NTT Docomo Note: LAA burst length 1/4/10 ms | 1)CCA-ED TL=-62dBm: 81~117% UPT gain with 2)CCA-ED TL=-82dBm; 84~170% UPT gain | 1)CCA-ED TL=-62dBm; 36~67% UPT gain 2)CCA-ED TL=-82dBm; 77~96% UPT gain | 1)CCA-ED TL=-62dBm; 12~49% UPT gain 2)CCA-ED TL=-82dBm; 70~89% UPT gain | 
[3] Samsung |  | 60% load 1) FBE: 5~12% UPT gain 2) LBE: 3~7% UPT gain 3) No LBT: 20~50% UPT loss |  | 
[4] ZTE |  | 1)30 MHz LAA UE bandwidth; 73% UPT gain 2)20 MHz LAA UE bandwidth; 31% UPT gain |  | Improved latency 0.4~0.6 times
[5] Cisco | DL only: Loss < 50% UL only: Loss > 25% No LBT | DL only: Loss = 100% UL only: Loss = 100% No LBT | DL only: Loss = 100% UL only: Loss = 100% No LBT | 
[6] Broadcom, CableLabs | Loss :14% ~62% (aggregate network throughput ) (WiFi: Data only or Voice+Data; LAA-LTE: Data only) |  |  | Degraded latency 4 ~8 times
The table shows the victim WiFi network’s thoughput gain or loss when an aggressor WiFi network is replaced by an aggressor LAA network.
Note that the traffic loads are not comparable across companies.

## Slide 7: Function assumptions
Source | LBT | LBE | FBE
Huawei | √ | √ | 
NTT Docomo | √ |  | 
Samsung | √ | √ | √
ZTE | √ |  | √
Cisco | × |  | 
Broadcom, CableLabs | √ |  | 
ETRI | √ |  | 

## Slide 8: Simulation Assumptions
Parameters | LAA-LTE | Wi-Fi
Scenario | Indoor Hotspot(1)(3)(6); Indoor Enterprise(5); Outdoor(2)(4) | 
System bandwidth per carrier on unlicensed band | 20MHz(1)(2)(4)(5)(6) | 
Carrier frequency for unlicensed band | 5.0GHz(1)(2)(4); 5.3GHz(5); 5.27GHz(6) | 
Carrier number (Y) | 1(1)(2)(4)(5)(6); 4 with carrier selection(3) | 
Num. of clusters/buildings per Macro area | Indoor: 1 building per macro cell(1)(3)(5)(6); Outdoor: 1 cluster per macro cell(2)(4) | 
Num. of cells per operator per cluster /building (X) | 2(1)(2); 4(3)(4)(5)(6) | 
UE dropping | Uniform and random: 10 per cell per operator(1); 40UEs per operator(3); 15 UEs per macro cell per operator(4); Range {2, 5, 10, 15, 20, 30}UEs per operator(5); 60UEs per operator network(6) | 
Pico/AP antenna configuration | 2D, Omni-directional: 1T2R(1); 2T2R(2)(5); 2T2R for LTE and 1T1R for Wi-Fi(4) | 
Cell antenna height | 6m for indoor(1)(5); 10m for outdoor(2)(4) | 
UE antenna height | 1.5m(1)(2)(4)(5) | 
Pico and AP DL Tx power | 18dBm(1)(3); 23dBm(2)(5); 30dBm(4) | 

## Slide 9: Simulation Assumptions
Parameters | LAA-LTE | Wi-Fi | 
Traffic model | FTP3 with packet size of 0.5Mbyts and various arrival rate(1); FTP1 with packet size of 0.5 Mbyts(2) FTP model 3 with 0.1 Mbyte file size(3); FTP3 with packet size of 0.1Mbyts and λ = 10(4); FTP3 with packet size of 0.5Mbyts and λ = 0.2Hz(5); 2 configurations(6): DL Data for Wi-Fi B/LAA and 1) Mixed traffic of 20% bidirectional voice+80% bidirectional data, 2) 100% DL data for Wi-Fi A, where UDP = 9.6Kbps/flow, packet size = 24 Bytes, arrival rate = 20ms for voice, UDP = 0.4Mbps/flow/direction. Packet size = 1500 Bytes for Wi-Fi |  | 
Scheduler algorithm | PF(1)(2)(4); Fair(5) |  | CSMA/CA-based, round robin(1)(2)
CCA busy threshold | -73 dBm/MHz + 23 - PH, PH in dBm EIRP(1)(4); -62dBm or -82dBm(2); No CCA implemented(5); CCA-ED with various threshold(6) |  | -62 dBm for CCA-ED, and -82 dBm for CCA-CS(1)(2)(3)(5) ; -73dBm/MHz + 23 - PH dBm (PH is e.i.r.p) dBm for CCA-ED, and -82 dBm for CCA-CS(4) ; CCA-ED with various threshold and CCA-CS with -92dBm threshold (6)
MCS | Up to 64 QAM(1)(2)(3) (4)(5) |  | Up to 64 QAM(1)(2)(3)(4) ; 256QAM included(5)
Length of extended CCA /CCA backoff | 1~32 CCA slots(1) |  | 15~1023 slots(1)(2)(3)(5) ; 16~64(4)
Max burst length | {1 ,4, 10} ms(2), 13ms(1) |  | 3ms(1); 4ms(2)(5); Not enabled(4)
Metric | SCT, UPT(1); UPT(2)(3)(5); UPT, Latency(4); SCT, Latency(6) |  |