## Slide 1: Proposals on SRS power allocation in dual connectivity
InterDigital, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, LG, Samsung
R1-145333
3GPP TSG RAN WG1 #79
San Francisco, USA, 17th – 21st November 2014
Agenda item 6.2.2.1

## Slide 2: Background
SRS power allocation in PCM1
  (For all options)
    SRS can only take power not used by PUCCH/PUSCH in last SC-FDMA symbol
  Option B1 (“option 1” in R1-145190)
    Maximum power of CG in last symbol containing SRS is at least the guaranteed power
    Same power allocation principle as for PUCCH/PUSCH is used for SRS in last symbol, but power allocation between CG’s may be different in last symbol
    SRS has least priority in remaining power, with tie-break to MCG (already agreed)
  Option A1 (“option 2” in R1-145190)
    Maximum power of CG in last symbol containing SRS is at least the guaranteed power
    Power allocation between CG is the same in last symbol containing SRS than in earlier symbols containing only PUCCH/PUSCH
    Dynamic power sharing is not supported for SRS, i.e. SRS may be scaled even if Pcmax would not be exceeded
  Option C1
    SRS has lower priority than PUCCH/PUSCH even for the guaranteed power
    Power allocation of PUCCH/PUSCH may be such that no power is available to SRS
    SRS of MCG has higher priority than SRS of SCG

## Slide 3: Background
SRS power allocation in PCM2
  Option A2 (“Option 1” in R1-145190)
    SRS power in a CG is limited by the allocated powers for PUCCH/PUSCH in the same CG
      FFS if SRS can have at least the guaranteed power
    SRS has lower priority than the other CG’s overlapping PUCCH/PUSCH transmission
    SRS power is computed at subframe boundary
  Option C2 (“Option 2” in R1-145190)
    SRS power in a CG can take all the remaining power (not taken by other CG at subframe boundary)
    SRS has higher priority than the other CG’s overlapping PUCCH/PUSCH transmission
    SRS power is computed at subframe boundary
  Option B2 (“Option 3” in R1-145190)
    SRS power in a CG is limited by the power allocated to the other CG in subframe overlapping with SRS
    SRS power is computed at last SC-FDMA symbol after power allocation for PUCCH/PUSCH transmissions (of any CG) started earlier is performed

## Slide 4: Proposal
In PCM1, dynamic power sharing is supported for SRS
  Guaranteed power (P_MeNB/P_SeNB) is applicable to SRS
  Same power allocation principle as for PUCCH/PUSCH is used for SRS in last symbol but power allocation between CG’s may be different in last symbol (option B1)
In PCM2, SRS has lower priority than the other CG’s PUCCH/PUSCH transmission starting earlier than SRS
  SRS power in a CG is limited by the power allocated to the other CG in subframe overlapping with SRS and starting earlier (option B2)

## Slide 5: (For information only) – expected specification impact (PCM1)
Option A1
Option B1
Option C1
In PCM1 power allocation (5.1.4.1)
In PCM1 power allocation (5.1.4.1)

## Slide 6: (For information only) – expected specification impact (PCM2)
Option A2
Option B2
Option C2
Modified formula in PCM2 power allocation (5.1.4.2)