## Slide 1: Observations on SIB Performance for MTC
Nokia Networks, Nokia Corporation
R1-145391
3GPP TSG RAN WG1 #79
San Francesco, USA, 17th – 21st Nov 2014
Agenda item 6.3.1.2.2

## Slide 2: Observations
RAN1 has considered the performance of SIB for Rel-13 low-complexity UE
  Simulation scenario – 10MHz system bandwidth, 1Rx antenna, 6 PRBs, EPA (1 Hz) channel, 1% BLER target
Based on simulation results provided in RAN1#79, it is seen that, for Rel-13 low complexity UE in normal coverage (SNR = -4dB)
  Repetition is required to transmit SIB messages
  The number of repetitions can be high
    e.g. 16-32 repetitions are required for SIB size of 328 bits
  The number of repetitions increases with the SIB size
    e.g. 16-32 repetitions are required for SIB size of 328 bits, 30-40 repetitions are required SIB size of 504 bits
  For a given SIB size, it may be more efficient to use one SIB rather than multiple smaller SIBs
    e.g. 40-80 repetitions are required for SIB size of 1000 bits, while 30-40 repetitions are required for SIB size of 504 bits

## Slide 3: Observations
Based on simulation results provided in RAN1#79, it is seen that, for Rel-13 low complexity UE in enhanced coverage (SNR = -14.3 dB)
  The number of repetitions can be very high
    e.g. 150 repetitions are required for SIB size of 328 bits
  The number of repetitions increases with the SIB size
    e.g. 100 repetitions are required for SIB size of 152 bits, 150 repetitions are required SIB size of 328 bits
  For a given SIB size, it may be more efficient to use one SIB rather than multiple smaller SIBs
    e.g. 160 repetitions are required for SIB size of 1000 bits, while 160 repetitions are required for SIB size of 504 bits [Note these results are for 10% BLER]
  Note that SIB results for UE in enhanced coverage are only from one company