## Slide 1: WF on LBT schemes for LAA
Ericsson, Qualcomm, NTT DOCOMO, Huawei, HiSilicon, Samsung, III, CHTTL,…
3GPP TSG RAN WG1 #80 R1-150785
Athens, Greece
9th – 13th February 2015
Agenda item: 7.2.3.1
Document for decision

## Slide 2: Background
All the LBT schemes that were considered for coexistence evaluations, fall into the following four categories:
  Category 1: No LBT
  Category 2: LBT without random backoff
    Examples: FBE type schemes
  Category 3: LBT with random backoff with fixed size of contention window
    Examples: LBE type schemes with or without defer periods
  Category 4: LBT with random backoff with variable size of contention window
    Examples: LBE type schemes with exponential increase of contention window

## Slide 3: Proposal
Classify the evaluated LBT schemes according to the following categories:
  Category 1: No LBT
  Category 2: LBT without random backoff
  Category 3: LBT with random backoff with fixed size of contention window
  Category 4: LBT with random backoff with variable size of contention window