## Slide 1: WF on Physical Channel Timing Relationships
Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, [Ericsson], [Sequans], [Sony], …
R1-154819
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.1.1

## Slide 2: Proposal
Timing relationships between M-PDCCH and PDSCH
  For UEs requiring no and >0 repetitions, cross-subframe (k>0) scheduling is supported.
  In CE, if a UE is configured with multiple M-PDCCH repetition factors ( e.g. corresponding to {4,8,16} repetitions), the PDSCH does not start before the end of the repetitions associated with the successfully decoded M-PDCCH candidate (e.g. 8 repetitions)
    This takes into account early decoding termination by UE, where UE is able to decode with fewer repetitions than actually used R; early termination allows UE to sleep

## Slide 3: Proposal
Timing relationships between M-PDCCH and PUSCH
  In FDD, the PUSCH starts in subframe n+4, where n is one of the following:
    Alt 1: n is the last subframe that belongs to the MPDCCH candidate set.
    Alt 2: n is the last subframe that belongs to the decoded M-PDCCH message for the UE (corresponding to the PUSCH)
Timing relationships between PDSCH and PUCCH
  In FDD, if PDSCH transmission ends in subframe n, PUCCH carrying HARQ-ACK starts in subframe n+k
    WORKING ASSUMPTION: k=4 as per legacy HARQ timing, but this can be revisited if significant issues are found.
    The UE can determine the end point of the PDSCH from the DCI
    FFS: For HD-FDD if multiple DL ACK/NACK responses are bundled over a PUCCH.