## Slide 1: WF on FD-MIMO codebook
Samsung, ZTE, ALU, ASB, Ericsson, CATT
R1-154861
3GPP TSG-RAN WG1#82
Beijing, China, August 24-28, 2015

## Slide 2: Proposal
For each of [8], 12 and 16 Tx ports, a precoding m in the codebook is represented as:
where:
  , FFS
  is a N1xL1 matrix with L1 column vectors being an O1x oversampled DFT vector of length N1:
  is a N2xL2 matrix with L2 column vectors being an O2x oversampled DFT vector of length N2:
  N1 and N2 are the numbers of antenna ports per pol in 1st and 2nd dim.
  FFS whether to select different beams (e.g. different X1 or X2) for the two pols
  FFS column selection from KP applied to W1

## Slide 3: Alt 1
Tall, [square] and wide arrays are supported with a single codebook for each of [8], 12 and 16 CSI-RS ports
  For PUSCH and PUCCH reporting, a codebook subset can be separately selected via RRC signaling of codebook subset selection parameters or a bitmap
  FFS beam subset selection/restriction and related mechanism
  FFS which and how the parameters below are related/configured
Parameter per dimension | Remark
Oversampling factors Od | Determines total number of beams Qd = Od · Nd, d = 1,2 in the codebook.
Beam group spacing | Difference of the leading beam indices of two adjacent beam groups
Number of beams in each beam group | May depend on rank and/or W1
Beam spacing | Difference of two adjacent beam indices in each beam group

## Slide 4: Alt 2
Tall, [square] and wide port layouts are supported with parameters N1, N2
  Values of N1 and N2 are RRC signaled
The parameters below define the codebook
  Configurable oversampling factors, RRC signaled, values FFS
  Other parameters are to be determined
  FFS beam subset selection/restriction and related mechanism
Parameter per dimension | Remark
Oversampling factors Od | Determines total number of beams Qd = Od · Nd, d = 1,2 in the codebook. The number of possible values for Od is FFS.
Beam group spacing | Difference of the leading beam indices of two adjacent beam groups
Number of beams in each beam group | May depend on rank and/or W1
Beam spacing | Difference of two adjacent beam indices in each beam group

## Slide 5: Alt 3
For each number of 12 and 16 CSI-RS ports, at most two fixed codebooks are specified in spec (with W1 design details FFS).
FFS: Reuse the same W2 as in Rel-12 codebook.
For PUSCH reporting, no subsampling is applied; for PUCCH reporting, subsampling can be applied

## Slide 6: Alt 4
For each number of 16 and 12 CSI-RS ports, a single fixed codebook is specified in spec
Only the total number of CSI-RS ports needs to be signaled
FFS: W1 and W2 design details
FFS: for PUSCH and PUCCH reporting

## Slide 7: Proposals
The number of bits on PUSCH/PUCCH CSI reports should be determined considering performance, overhead and UE complexity.
Down-select or merge the 4 alternatives into one in the next meeting
  Including necessary RRC parameters