## Slide 1: WF on DL LBT priority classes
Ericsson, Huawei, HiSilicon, NTT DOCOMO …
3GPP TSG RAN WG1 #82 R1-154993
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Proposal
A category 4 LBT priority class is defined by the minimum and maximum contention window (CW) sizes and the number of CCA slots in the defer period (n in Table below).
In Rel13 for a DL burst transmission containing PDSCH, an LAA SCell operates with a single category 4 LBT priority class at a time when performing random backoff.
Best effort traffic uses the LBT priority class 3.
LBT priority class | CWmin | CWmax | n
1 | 3 | 7 | 1
2 | 7 | 15 | 1
3 | 15 | 63 | 3
4 | 15 | 1023 | 7

## Slide 3: Proposal (cont.)
If an intended DL transmission burst with PDSCH contains traffic corresponding to different LBT priority classes, the lowest priority shall be used for the LBT parameters.
FFS if more LBT priority classes are needed.
Inform RAN2