## Slide 1: WF on Narrowbands for MTC-SIB1 frequency hopping
NEC, InterDigital, Qualcomm, NTT DOCOMO, ZTE, Intel, Sierra Wireless,
3GPP TSG RAN WG1 Meeting #82bis
Malmo, Sweden, 5th - 9th Oct 2015
Agenda Item: 7.2.1.1
R1-156119

## Slide 2: Background
Confirm working assumption: At least in case the network supports enhanced coverage, frequency hopping for MTC-SIB1 is always used at least system bandwidth >= 5MHz.
  Option A: MTC-SIB1 frequency hopping takes place between 2 narrowbands in the cell.
  Option B: MTC-SIB1 frequency hopping takes place between 2 or 4 narrowbands as indicated in MIB.
  Working assumption: The mentioned narrowbands are determined based on cell ID and system bandwidth.
  Working assumption: The hopping sequence between these narrowbands is determined based on cell id and subframe index (and/or SFN).

## Slide 3: Proposals
MTC-SIB1 frequency hopping takes place between 2 or 4 narrowbands depending on the system bandwidth
    narrowbands = 2 for system BW of 12-50 RBs
    narrowbands = 4 for system BW of 51-110 RBs
Confirm the working assumption that the mentioned narrowbands are determined based on cell ID and system bandwidth
    FFS on how to handle the case if MTC-SIB1 overlaps with PBCH
Confirm the working assumption that the hopping sequence between these narrowbands is determined based on cell ID and subframe index (and/or SFN)