## Slide 1: WF on UL/DL HARQ for MTC
Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Intel, Qualcomm
R1-156174
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th - 9th October 2015
Agenda item 7.2.1.1

## Slide 2: Background
Agreements:
  For HD-FDD, FD-FDD, and TDD, if the UE is operating with coverage enhancement (but not small one):
    UE is expected to support no more than N DL HARQ process to receive unicast PDSCH
      FFS N=1, 2, or 4
    UE is expected to support no more than M UL HARQ process to transmit PUSCH
      FFS M = 1, 2, 4, or Rel-8 # of UL HARQ processes
  For HD-FDD, FD-FDD and TDD, if the UE is operating with no repetition, the same max number of DL and UL HARQ processes as for Cat-0 UE in Rel-12, except that:
    FFS if the number of DL HARQ processes should be increased for TDD with respect to that of Rel-8 for the case of no repetition
  FFS the case of small coverage enhancement
  Soft buffer management is based on a maximum of 8 DL HARQ processes as in Rel-8
  PUSCH HARQ feedback is realized using M-PDCCH
    Note that this does not preclude HARQ feedback to multiple UEs by single M-PDCCH

## Slide 3: Proposal
For HD-FDD, FD-FDD, and TDD, if the UE is operating with medium-to-large coverage enhancement
  UE is expected to support no more than N=2 DL HARQ processes to receive unicast PDSCH
  UE is expected to support no more than M=2 UL HARQ processes to transmit PUSCH
PDSCH HARQ operation for LC/CE UEs is asynchronous and adaptive
  This is the same as in legacy operation
PUSCH HARQ operation for LC/CE UEs is synchronous
  At least adaptive PUSCH HARQ retransmission is supported for LC/CE UEs
  Whether to also support non-adaptive PUSCH HARQ retransmission for LC/CE UEs is FFS