## Slide 1: 3GPP TSG RAN WG1 Meeting #82bis R1- 156187 Malmo, Sweden, October 5-9, 2015 Agenda item 7.2.1.1
WF on HARQ process number for MTC UEs operating CE
Huawei, HiSilicon, ……

## Slide 2: Background
Agreement:
For HD-FDD, FD-FDD, and TDD, if the UE is operating with coverage enhancement (but not small one):
  UE is expected to support no more than N DL HARQ process to receive unicast PDSCH
    FFS N=1, 2, or 4
  UE is expected to support no more than M UL HARQ process to transmit PUSCH
    FFS M = 1, 2, 4, or Rel-8 # of UL HARQ processes
For HD-FDD, FD-FDD and TDD, if the UE is operating with no repetition, the same max number of DL and UL HARQ processes as for Cat-0 UE in Rel-12, except that:
  FFS if the number of DL HARQ processes should be increased for TDD with respect to that of Rel-8 for the case of no repetition
FFS the case of small coverage enhancement
Soft buffer management is based on a maximum of 8 DL HARQ processes as in Rel-8

## Slide 3: Proposals (1)
For HD-FDD and FD-FDD, if the UE is operating with coverage enhancement:
  UE is capable of supporting max N DL HARQ process to receive unicast PDSCH
    N = 4
  UE is capable of supporting max M UL HARQ process to transmit PUSCH
    M = 4

## Slide 4: Proposals (2)
For TDD, if the UE is operating with coverage enhancement:
  UE is capable of supporting max N DL HARQ process to receive unicast PDSCH
    N = 4
  Working assumption: UE is capable of supporting max M UL HARQ process to transmit PUSCH
    M = 4
    Confirm working assumption unless the RTT for this case is a concern