## Slide 1: Way forward on observations of link-level simulation results for MUST Cat. 1 & 2
MediaTek, CHTTL, ZTE
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.7.2
R1-156201

## Slide 2: Background
  The observations are drawn from the following link-level simulation results based on the agreed link-level evaluation assumptions
    R1-155700 (MediaTek), R1-155324 (Intel), R1-155408 (LG), R1-155640 (Huawei), R1-153822 (Alcatel-lucent), R1-154537 (NTT DoCoMo), R1-154058 (ZTE)

## Slide 3: Observations (1/2)
  For the MUST-near user:
    In MUST category 1, ML receiver can achieve similar link-level performance as ideal CWIC receiver when the MUST-far user uses QPSK and holds high transmission power ratio (e.g. > 0.8)
    In MUST category 2, ML receiver can achieve similar link-level performance as ideal CWIC receiver when MUST-far user uses QPSK
    Considering ML receiver, MUST category 2 shows similar link-level performance to MUST category 1 when the MUST-far user uses QPSK modulation and when the MUST-far user holds high transmission power ratio (e.g. > 0.9)
    Considering ML receiver, MUST category 2 outperforms MUST category 1 in link-level performance when the MUST-far user holds smaller transmission power ratio (e.g.  0.8) or the MUST-far user uses 16QAM or higher modulation order

## Slide 4: Observations (2/2)
For the MUST-far user:
  In MUST category 1, MMSE receiver can achieve similar link-level performance as ML receiver when the MUST-far user uses QPSK
  In MUST category 2, MMSE receiver can achieve similar link-level performance as ML receiver
  Considering MMSE receiver, some schemes of MUST category 2 (e.g. R1-154184, R1-154454) can outperform MUST category 1 in link-level performance when the MUST-far user uses 16QAM or higher modulation order or when the MUST-far user holds smaller transmission power ratio (e.g. < 0.6)