## Slide 1: WF on SIB1bis Transmission
Nokia Networks, Ericsson, Samsung, Panasonic, NEC, LGE, Intel, InterDigital, CATT, Sierra Wireless, MediaTek
R1-156262
3GPP TSG RAN WG1 #82bis
Malmö, Sweden, 5th - 9th October, 2015
Agenda item 7.2.1.6

## Slide 2: Background
Agreements from RAN1#81
  The number of resource blocks used for MTC SIB transmission is fixed to 6 PRBs.
  Scheduling information for MTC SIB1
    TBS of MTC SIB1 is based on information in the MIB.
    Frequency location of MTC SIB1 is derived from at least PCID.
    Time location
      Possible subframes are {0,4,5,9} for FDD and {0,5} for TDD. FFS subframes {1,6} for TDD.
      FFS: Whether the subframes and frames are signaled in MIB and/or fixed/predefined in specification.
  Scheduling information for MTC SIBs other than MTC SIB1 are given in MTC SIB1.
  The number of repetitions for MTC SIBs other than MTC SIB1 is configurable by the network.
    FFS: MTC SIB1.
    FFS: How the network will signal the number of repetitions
  FFS: For MTC SIB1 transmission, subframes #1 and #6 are used

## Slide 3: Background
Agreements from RAN1#82
  At least in case the network supports enhanced coverage, frequency hopping for MTC-SIB1 is always used at least system bandwidth >= 5MHz.
    Option A: MTC-SIB1 frequency hopping takes place between 2 narrowbands in the cell.
    Option B: MTC-SIB1 frequency hopping takes place between 2 or 4 narrowbands as indicated in MIB.
    Working assumption: The mentioned narrowbands are determined based on cell ID and system bandwidth.
    Working assumption: The hopping sequence between these narrowbands is determined based on cell id and subframe index (and/or SFN).
  MTC-SIB1 repetition - for SI transmission:
    At least the following are predefined or derived from MIB:
      (a) periodicity of MTC-SIB1 transmission
      (b) repetition number within the periodicity of MTC-SIB1 transmission

## Slide 4: Proposals (1)
SIB1bis is transmitted periodically with a period of TSIB1bis radio frames
  Within a period, SIB1bis can be repeated a number of times
  RV cycling {0,2,3,1,…} is used for each SIB1bis transmission within a period
For TDD, subframes #1 and #6 are not used for SIB1bis transmission
SIB1bis content does not change over X*TSIB1bis radio frames

## Slide 5: Proposals (2)
SIB1bis transmission period TSIB1bis is predefined
  TSIB1bis = [8] radio frames
Repetition number RSIB1bis within a period is derived from MIB
Time location is determined by
  First transmission of SIB1bis is transmitted in subframe #5 of radio frames for which the SFN mod TSIB1bis = 1
  For repetitions, FFS
    Option 1: Time location for repetitions is determined from RSIB1bis, PCID and SFN
    Option 2: Time location for repetitions is determined from RSIB1bis
Frequency location is determined by
  Narrowband for first transmission of SIB1bis is given by PCID modulus number of narrowbands in the downlink system bandwidth
    FFS: How to handle collision with P-BCH
  Narrowband for repetitions is determined by a hopping pattern
    WA: hopping pattern is 80ms
    FFS details of the hopping pattern and whether to consider RSIB1bis