## Slide 1: WF on Same Subframe Scheduling
Sony, InterDigital, CATT, Lenovo, Sierra Wireless
R1-156288
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th – 9th October 2015
Agenda item 7.2.1.1

## Slide 2: Background
Working assumption from RAN1#82
  Same-subframe scheduling for PDSCH (i.e., the one associated with an M-PDCCH in the same subframe) for LC-MTC UEs is NOT supported
    Can revisit if significant issues are found especially regarding the number of HARQ processes
Agreement from RAN1#82
  For HD-FDD, FD-FDD and TDD, if the UE is operating with no repetition, the same max number of DL and UL HARQ processes as for Cat-0 UE in Rel-12, except that:
    FFS if the number of DL HARQ processes should be increased for TDD with respect to that of Rel-8 for the case of no repetition
Agreement from RAN1#82bis
  For DL cross-subframe scheduling Case 1 without repetition and with repetition, PDSCH (new and re-transmissions) starts from the second valid downlink subframe after the end of the corresponding transmitted M-PDCCH with the given repetition level
    FFS whether there is impact of UL scheduling for HD-FDD and if so, how, etc.
With 8 PDSCH HARQ processes and PDSCH starting from 2nd valid downlink subframe after end of MPDCCH, UE is unable to achieve peak throughput

## Slide 3: Background
To achieve peak throughput in
  FD-FDD
    Increase the number of HARQ processes from 8 to 10
    Enable same subframe scheduling
  HD-FDD
    Increase the PDSCH and PUCCH (ACK/NACK) timing from k=4 to k=5
    Introduce ACK/NACK bundling
    Enable same subframe scheduling

## Slide 4: Proposal
Same-subframe scheduling for PDSCH (i.e., the one associated with an M-PDCCH in the same subframe) for LC-MTC UEs is supported for no repetition scenario