## Slide 1: Proposal on power-control parameters for new PUCCH formats
NTT DOCOMO, INC.
R1-156364
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.2.1.1

## Slide 2: Proposal
RAN1 to conclude following selection.
  Option 1: Power-control formula of PUSCH-like new PUCCH format without CDM and with CDM is based on PUSCH power-control formula.
  Option 2: Power-control formula of PUSCH-like new PUCCH format without CDM and with CDM is based on PUCCH power-control formula.

## Slide 3: Option 1: PUSCH-based
For the PUSCH-like new PUCCH format without and with CDM, following power-control formula is used.
  PO_PUCCH,c is the parameter which ranges (-127 … -96) replacing PO_PUSCH,c(j) in the PUSCH power-control formula.
  For DeltaTF,c(i),
    Ks is fixed to 1.25.
    Beta-offset is fixed to a certain FFS value.

## Slide 4: Option 2: PUCCH-based
For the PUSCH-like new PUCCH format without and with CDM, following power-control formula is used.
Confirm the following working assumption.
  For the power-control of the PUSCH-like new PUCCH format,
    DF_PUCCH(F) is included, where DF_PUCCH(F) is higher-layer configured PF-dependent power offset.
      For the DF_PUCCH(F), one of up to 8 values is configured by higher-layers.
      FFS: Exact values.