## Slide 1: WF on Periodic CSI reporting configuration
Nokia Networks, Lenovo, Samsung, Ericsson, NTT DOCOMO, Huawei, HiSilicon, Intel, LGE, NEC
3GPP TSG RAN WG1 #82bis R1-156372
Malmö, Sweden
5th – 9th October 2015
Agenda item: 7.2.2.1.3
Document for decision

## Slide 2: WF on configuration of P-CSI reporting - periodic CSI-only
Per-CC configuration of periodic CSI (up to 32 CCs) as rel-12
  Reporting mode, periodicity, subframe offset (separately for RI and CQI/PMI), PUCCH format 2 resource as in Rel-12
  The existing per-CC P-CSI configuration is extended to support up to 32 CCs
Up to two At least one (FFS more than one) UE specific configuration(s) for multi P-CSI transmission (“multi P-CSI resource ”), each including the following
  PUCCH Format (new PUSCH-like PUCCH format, FFS: new PUSCH-like format with CDM, FFS: format 3)
  PUCCH Resource
  Max supported payload [bits or reports] or code rate, up to 8 32 RRC signaling states
    If the maximum is exceeded, the UE drops reports according to priority rules (Rel-12 rules as a baseline) until supported payload is not exceeded
  [Power control related parameters, common config for all UCI types]
In a subframe where only one periodic CSI occurs, PUCCH format 2 is used as in Rel-12
In a subframe where more than one periodic CSI occur, one of the multi P-CSI resource(s) is used
  FFS how to select one of the multi P-CSI resource(s)

## Slide 3: WF on configuration of P-CSI reporting - periodic CSI + HARQ-ACK/SR
FFS how to define a maximum number of CSI + HARQ-ACK/SR bits to be transmitted in one new PUSCH-like PUCCH resource in a subframe