## Slide 1: WF on spatial consistency
Intel, InterDigital, Huawei, HiSilicon, Qualcomm, Ericsson, LGE, Nokia, Alcatel Shanghai Bell, NTT DoCoMo, Samsung, CATT, ETRI, Lenovo, Motorola Mobility, NTT, ZTE, AT&T
R1-163475
3GPP TSG RAN1 #84b
Busan, Korea, April 11 - 15, 2016
Agenda Item: 8.2.3.2

## Slide 2: Background
In RAN1 ad hoc on Channel modeling, spatially consistent random number based approach (R1-161726) is agreed as working assumption for spatial consistency modeling
  The working assumption is sufficient for drop based MU-MIMO simulation

## Slide 3: Proposal
Confirm the working assumption of R1-161726 as agreement for drop based MU-MIMO simulations
  The correlation distance for cluster/ray specific random variables is according to table below
  The correlation distance for LoS state and indoor/outdoor state is [50m] for UMa and [50m] for UMi
  The correlation distance for LoS state of Indoor scenario is [10m]
 | UMi |  |  | UMa |  |  | Indoor
 | LOS | NLOS | O-to-I | LOS | NLOS | O-to-I | 
Correlation distance (m) for cluster specific random variables | [12] | [15] | [15] | [40] | [50] | [15] | [10]