## Slide 1: Discussion on removal of square bracket for cluster level SSP
Huawei, HiSilicon
R1-165460
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23 - 27 May, 2016
Agenda Item: 7.2.2

## Slide 2: Background
For current results collected from different companies in R1-163472, the number of clusters are small and around 4.
Some concerns are raised in Busan meeting and also Nanjing meeting on a smaller cluster number than IMT-A model.
To facilitate the full calibration and also the completion of the SI, it is proposed that for indoor office, the number of cluster and number of rays per cluster could be increased.
Based on the new value on the number of cluster and number of rays per cluster, the scaling factor for generating the angular domain channel should also be provided.

## Slide 3: Proposal
the number of cluster and number of rays per cluster in table 1 will be adopted for indoor office. And the square bracket can be removed.
Scenarios | LOS | NLOS
Number of cluster | 8 | 10
Number of rays per cluster | 20 | 20
The scaling factors,
  For the AoA and AoD, the scaling factor for UMi and UMa can be reused for indoor office.
  For the ZoA and ZoD, the results in table 2 will be adopted for indoor office .
Table 1 SSP for indoor office (part)
Scaling factors for ZOA/ZOD |  | 
Number of cluster | 8 | 10
C | 0.889 | 0.957
Table 2 scaling factor for indoor office