## Slide 1: WF on scaling of subcarrier spacing in NR
Samsung, Intel, KT Corp.,
Verizon Wireless, Fiberhome
3GPP RAN1#85
Nanjing, China, 23 – 27 May 2016
Agenda: 7.1.4
R1-165517

## Slide 2: Background
Agreement in last RAN1#84bis:
RAN1 will continue further study and conclude between following alternatives in the next meeting
Alt. 1
  fsc = f0 * 2m
  where f0 is FFS and m is an integer chosen from a set of possible values.
Alt. 2
  fsc = f0 * M
  where f0 is FFS and M is an integer chosen from a set of possible positive values.

## Slide 3: Observation
Subcarrier spacing should be decided by considering various aspects, e.g., usage scenario, deployment scenario, performance requirements, and etc.
  2m scalability in Alt. 1 may not be sufficient and future-proof.
R1-164179
R1-163984

## Slide 4: Proposal
  fsc = f0 * M (Alt. 2) should be taken into account as the scaling method of subcarrier spacing in NR SI where f0 = 15 kHz.
  Subcarrier spacing values to be studied in NR SI include at least
  {15, 30, 60, 75, 120, 150, 240, 300} kHz