## Slide 1: Way Forward on priority information in SCI
3GPP TSG RAN WG1 Meeting #85 R1-165561
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 6.2.2.2.4
Huawei, HiSilicon, Intel, Ericsson, Sharp, LG Electronics, NTT DoCoMo, OPPO , ITRI, Kyocera, Nokia, ASB, Potevio

## Slide 2: Background
Agreements on priority handling in RAN1 #84bis:
  Proposal 1:
    Priority handling is supported over PC5 for eNB-scheduled and UE- autonomous V2V communication
  Proposal 2:
    The priority information is taken into account in the resource (re)selection for UE-autonomous mode
      Further details are FFS
  Proposal 3:
    Down-select between two alternatives at RAN1#85 meeting
      Alt.1 Priority information is signaled in SCI
      Alt.2 Priority information is not signaled in SCI

## Slide 3: Proposal
Priority information is explicitly indicated by SA
  The number of bits is FFS.
  SCI decoding is used to identify associated data transmissions priority
If UE with lower priority transmission decodes a SCI with priority information higher than itself, UE doesn’t transmit on that resource and (re)select other resource.
  FFS if additional criteria is needed