## Slide 1: WF on general SRS aspects
Huawei, HiSilicon, …
3GPP TSG RAN WG1 #85 R1-165572
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.2
Document for decision

## Slide 2: background
Progress in RAN1 84bis meeting
Working assumption: Periodic SRS without PUSCH is NOT supported in Rel-14 eLAA WI
Agreements: Only wideband SRS transmission in supported in eLAA
  Existing max # SRS RBs for a given system bandwidth is the baseline
    FFS whether or not to extend/shift to # of RBs > max # RBs in the legacy case
Working assumption: SRS is based on legacy comb structure
  As a baseline, comb = 2 and 4
  FFS whether or not support different comb value(s)

## Slide 3: Proposal
Confirm the following working assumptions
  Periodic SRS without PUSCH is NOT supported in Rel-14 eLAA WI
  SRS is based on legacy comb structure
    As a baseline, comb = 2 and 4
Additional comb values are not supported
Keep the existing max # SRS RBs for a given system bandwidth
  To cover the whole system bandwidth, the starting PRB index of the SRS is determined from the subframe index
    5 starting PRB indices for 96 PRB SRS
    3 starting PRB indices for 48 PRB SRS
Remove cell-specific and UE-specific SRS subframe configuration in RRC signaling