## Slide 1
3GPP TSG RAN WG1 Meeting #85 R1-165642 Nanjing, China, 23rd - 27th May 2016
Agenda item: 7.1.6
WF on Beamformed CSI-RS
Huawei, HiSilicon, CATT, …

## Slide 2: Background
Until RAN1#85, down-selection/merge the following alternatives for reducing
the overhead for beamformed CSI-RS, considering overhead reduction,
performance, backward compatibility, UE implementation complexity:
  Alt.1: Aperiodic CSI-RS
    E.g., One-shot CSI-RS transmission with transmission on the same subframe as triggering subframe
  Alt.2: Dynamic CSI-RS activation and/or deactivation
    E.g., One-shot or multi-shot CSI-RS transmission after the triggering subframe
  Alt.3: Reduced frequency density via decimation over part or all of the bandwidth
  Alt.4: MR with dynamic sharing of the beams on CSI-RS resources among the UEs
  Alt.5: Triggered measurement of one of multiple CSI-RS configurations
  Alt.6: Spatially multiplexed beamformed CSI-RS
  Other approaches are not precluded

## Slide 3: Proposal
Specify dynamic triggering of CSI-RS transmission on time domain including:
  At least Alt.1: At least single shot Aperiodic CSI-RS
    CSI request in UL grand is reused for indication of A-CSI-RS
    FFS: multi-shot CSI-RS transmission once triggered
    FFS: signalling for resource allocation
  FFS: The combination with other alternatives (e.g. Alt3, Alt.4).
  Specify dynamic PDSCH rate matching indication
  Enhanced TM(s) is FFS