## Slide 1: WF on eLAA UL/DL scheduling combinations
Nokia, Alcatel-Lucent Shanghai Bell, CATT, LG Electronics, NTT DOCOMO, Qualcomm, Intel, Ericsson, ZTE, Fujitsu, ETRI, ITL, Huawei, HiSilicon, Samsung, Kyocera, Panasonic
3GPP TSG RAN WG1 #85
Nanjing, China, May 23rd-27th, 2016
R1-165647
Agenda 6.2.1.1

## Slide 2: Background from SI phase (TR)
Four possible scheduling combinations for an LAA SCell are identified below.
Combination 1: Self-scheduling on both DL and UL
Combination 2: Self-scheduling on DL and cross-carrier scheduling on UL
Combination 3: Cross-carrier scheduling on DL and self-scheduling on UL
Combination 4: Cross-carrier scheduling from the same scheduling carrier for both DL and UL
The LTE design in Rel-12 supports combinations 1 and 4 above. In addition, it has been identified that for the case with uplink self-scheduling where the UE applies a LBT procedure before transmitting on the UL, two successful LBT operations are required before the UE transmits on the UL. This is because, first the eNB performs an LBT procedure for an LAA SCell to send the scheduling command, and if this is successfully received by the UE, the UE performs an LBT procedure before transmitting in UL. Therefore, it could be beneficial to support scheduling combination 2 above in addition to combinations 1 and 4 which are already supported in LTE. In contrast, no clear use case has been identified for combination 3. Therefore, it is recommended that combination 3 should not be a design target for LAA. It can be further considered whether combination(s) 1, 2, and 4 should all be supported or some of them should be supported.

## Slide 3: Background on DCI monitoring
We assume the following to be valid for the LAA UL grant design:
  UE does separate BDs for DCI Format 1A and the new LAA UL grant formats (i.e. DCI Format 0A/0B and DCI 4A/4B if configured with UL TM2) respectively.
  Notes:
  DCI format 0A/4A: DCI format for single subframe scheduling with TM1/2
  DCI format 0B/4B: DCI format for multi-subframe scheduling with TM1/2
  There may be no differentiation of DCI formats for single subframe and multi-subframe scheduling in the end.
Therefore, the monitoring for UL and DL grants would have separate blind decodes and a logical separation for different UL and DL scheduling cell becomes possible

## Slide 4: Proposals
Support UL/DL Scheduling Combination 2: Self-scheduling on DL and cross-carrier scheduling on UL
  The UE to monitor for DCI formats scheduling PUSCH of a single eLAA Scell on one UL licensed-band scheduling cell
    i.e. DCI formats 0A/0B, Formats 4A/4B if configured for TM2
    Notes:
      DCI format 0A/4A: DCI format for single subframe scheduling with TM1/2
      DCI format 0B/4B: DCI format for multi-subframe scheduling with TM1/2
      There may be no differentiation of DCI formats for single subframe and multi-subframe scheduling.
  The UE to monitor for DCI formats scheduling LAA PDSCH on the LAA SCell
    i.e. DCI formats 1A/1B/1D/1/2A/2/2B/2C/2D
  Configuration details of enabling self-scheduling on DL and cross-carrier scheduling on UL are up to RAN2
  FFS: If UCI cell groups concept is agreed, then whether scheduling is allowed from outside the UCI cell group
  FFS: Whether cross-carrier transmissions of DCI scheduling on the UL is only applicable to PUSCH scheduling or whether it may be applicable to all the UL DCIs for the UL (e.g. if agreed, DCI for SRS triggering etc).
  FFS: How to manage the number of blind decodes at the UE side in general (equally applicable for other scheduling combinations)?