## Slide 1: WF on resource pool configuration
Huawei, HiSilicon, ZTE, NTT DoCoMo
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23rd - 27th May, 2016
AI: 6.2.2.4
R1-165755

## Slide 2: Background
In Rel-12 D2D, a resource pool is (pre)configured on a per-cell basis.
For V2V
  Frequency domain
    Data pool configured as non-adjacent clusters may be unnecessary for dedicated V2V carrier.
    Consecutive frequency resources can be configured by Rel-12 data pool configuration.
  Time domain
    Messages from multiple vehicles are generated randomly. If these messages are squeezed into a pool with unified starting and ending boundaries like Rel-12 D2D, it could cause unnecessary collisions and/or latency especially for large number of vehicles.
    UE can perform resource selection when a TB arrives (mode-2) or transmit when instructed by the eNB (mode-1).

## Slide 3: Proposal
  For PC5-based V2V, time domain resource pool can be (pre)configured.
  For PC5-based V2V, frequency domain resource pool can be (pre)configured.
  UE can perform resource selection when a TB arrives (mode-2) or transmit when instructed by the eNB (mode-1).