## Slide 1: WF on subcarrier spacing in NR
Verizon Wireless, KT Corp., Reliance-jio, CHTTL, China Telecom, Samsung, Intel, Potevio, Fiberhome, IITH, CEWiT, Tejas Neworks, Straight Path, ITL, WILLUS
3GPP RAN1#85
Nanjing, China, 23 – 27 May 2016
Agenda: 7.1.4
R1-165891

## Slide 2: Observation (1)
  During offline/online discussions, there have been strong request from some operators on NR to support different/diverse component carrier BWs
  Including 100 MHz and 200 MHz for eMBB
  It is important that subcarrier spacing support sufficient scalability/granularity

## Slide 3: Observation (2)
fsc = f0 * 2m (f0 =15kHz) is not efficient in terms of resource utilization when supporting 100 MHz CC BW
fsc = f0 * 2m (f0 =15kHz) has limited scalability to support 100 MHz, e.g. common resource allocation, filter design.
Scaling factor (M) | M=4 | M=5 | M=4 | M=4
Subcarrier spacing (kHz) | 60 | 75 | 60 | 60
Component carrier bandwidth (MHz) | 80 | 100 | 100 | 100
Total subcarrier bandwidth (MHz) | 72 (1200sc) | 90 (1200sc) | 72 (1200sc) | 90 (1500sc)
Guardband Ratio | 10% | 10% | 28% (Overhead) | 10%
OFDM symbol length (usec) | 16.67 | 13.33 | 16.67 | 16.67
No. of symbols/subframe | 14 | 14 | 14 | 14
Subframe length (ms) | 0.25 | 0.2 | 0.25 | 0.25
CP overhead | 6.57% | 6.57% | 6.57% | 6.57%
FFT Size | 2048 | 2048 | 2048 | 2048
Sampling rate (MHz) | 122.88 | 153.6 | 122.88 | 122.88

## Slide 4: Proposal
Take the following as working assumptions on subcarrier spacing:
  Working assumptions
    RAN1 concludes on alternative 1 (15 kHz) as the baseline design assumption for the NR numerology
    RAN1 concludes on scale factors N =2n for subcarrier spacing as the baseline design assumption for the NR numerology
    RAN1 include 75 kHz for subcarrier spacing as the additional baseline design assumption for the NR numerology