## Slide 1: WF on the determination of LBT priority class at the UE
Nokia, Alcatel-Lucent Shanghai Bell, …
3GPP TSG RAN WG1 #85
Nanjing, China, May 23-27, 2016
R1-165897
Agenda 6.2.1.5

## Slide 2: Proposal
The eNB is responsible for making sure that the ultimate mapping between QCI and LBT priority class is consistent with section 5.7.1 in TS 36.300.
  The eNB is allowed to assign a LBT priority class with lower priority compared to what is defined in section 5.7.1 in TS 36.300.

## Slide 3: Proposal
eNB signals the LBT priority class to the UE, UE performs LBT using the signaled priority class.
  There is no additional restriction at the UE (other than the multiplexing rules defined in RAN2) on the type of the traffic that can be carried in the scheduled subframes.
  eNB should not schedule the UE more subframes than what is needed to transmit all the traffic with the same LBT priority class or higher than the signaled LBT priority class based on the latest BSR.