## Slide 1: WF on PUCCH retuning for BL/CE UE
Ericsson, Qualcomm, NEC, Sequans, Virtuosys, Softbank, NTT DoCoMo, Sierra Wireless, CATT, Sony, Altair, LG Electronics, InterDigital, Huawei, HiSilicon, Verizon, AT&T, ZTE
R1-165903
AI 6.1.5
3GPP TSG RAN WG1 Meeting #85
Nanjing, China 23rd - 27th May 2016

## Slide 2: Background
The currently specified way to create guard periods during PUCCH retuning through rate matching has the following issues (see also R1-165869):
  PUCCH rate matching mismatch between UE and eNB in case of MPDCCH misdetection
  Ambiguous PUCCH transmission format in case the PUCCH transmission is followed by a SR resource allocation
  Larger implementation impact of rate matching compared to puncturing
  No possibility to exploit the fact that some UE implementations may be able to retune faster than 2 SC-FDMA symbols (e.g. 1 or 0 symbols)
  Time line impact for the case of PUCCH transmission after SPS release
Creating the guard periods during PUCCH retuning through puncturing instead of rate matching is expected to provide sufficient performance (see R1-157472).

## Slide 3: Proposal
Revoke the following RAN1#84 agreement:
  Shortening of PUCCH 1/1a/1b in the first slot of a subframe is realized by using in the first slot with PUCCH 1/1a/1b resource mapping from symbols 1 through 6 in the first slot while maintaining the existing PUCCH 1/1a/1b DM-RS locations.
Agree the following proposal:
  For PUCCH 1/1a/1b, UL retuning gaps are generated by puncturing of the affected SC-FDMA symbols: last symbol and first symbol of the prior and the latter subframe respectively
    However, if the prior subframe is an SRS subframe, shortened format of legacy behaviour is applied, i.e., shortened format is applied in the prior subframe, and first symbol of the latter subframe is punctured.