## Slide 1: WF on time interval X
Huawei, HiSilicon, Qualcomm, Nokia, ASB
3GPP TSG RAN WG1 #85 R1-166013
Nanjing, China, May 23 - 28, 2016
Agenda item: 7.1.4

## Slide 2: Background
Agreements:
At least the following should be supported for NR in a frequency portion
  A time interval X which can contain one or more of the following
    DL transmission part
    Guard
    UL transmission part
  FFS which combinations are supported and whether they are indicated dynamically and/or semi-statically
  Furthermore, the following is supported
    The DL transmission part of time interval X to contain downlink control information and/or downlink data transmissions and/or reference signals
    The UL transmission part of time interval X to contain uplink control information and/or uplink data transmissions and/or reference signals

## Slide 3: Proposals
At least the following combinations for time interval X should be supported
  Combination 1: A DL transmission part, a possible guard
  Combination 2: A possible guard, an uplink transmission part
  Combination 3: A DL transmission part, guard(s), and an UL transmission part