## Slide 1: WF on system level simulations for V2X NR
Ericsson
3GPP TSG RAN WG1 Meeting #86 R1-167932
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item: 8.1.7

## Slide 2: Background
The European Commission has allocated 1GHz of spectrum at 63GHz for ITS applications [1]
  V2X simulation assumptions should include such scenario.
Omnidirectional antenna arrays are unlikely to be deployed on NR vehicles/RSUs
  Furthermore, simulation assumptions should clarify the shape of the antenna array(s)

## Slide 3: Proposals on 63GHz
Add 63GHz carrier frequency with 1GHz bandwidth (63-64GHz) for UE-UE and for UE-RSU [1]
FFS UE-UE and UE-RSU channel models at 63GHz
40dBm e.i.r.p. Tx power limitation at 63GHz

## Slide 4: Proposal on antenna pattern at RSU
Revise the assumptions on RSU antenna pattern.
  4 antenna arrays with 2 elements each
  The arrays point to the 4 streets in the intersection
  Each antenna element irradiates with halfspherical uniform distribution over a 90deg azimuth angle
  Antenna gain = 9dBi

## Slide 5: Proposal on antenna pattern at vehicle UE
Revise the assumptions on vehicle UE antenna pattern.
Alt.1:
  4 antenna arrays with 2 elements each
  The arrays point to the front,rear,left,right
  Each antenna element irradiates with halfspherical uniform distribution over a 90deg azimuth angle
  Antenna gain = 9dBi
Alt.2:
  2 antenna arrays with 4 elements each
  The arrays point to the front, rear.
  Each antenna element irradiates with halfspherical uniform distribution over a 180deg azimuth angle
  Antenna gain = 6dBi
Collect input from automotive companies in
3GPP regarding preference between Alt.1/2

## Slide 6: Reference
[1] The European Commission. Commission implementing decision of 11 December 2013 amending decision 2006/771/EC on harmonisation of the radio spectrum for use by short-range devices and repealing decision 2005/928/EC.