## Slide 1: WF on Scalable Numerology Symbol Boundary Alignment
Qualcomm Inc.
3GPP TSG RAN WG1 #86 R1-167958
Gothernburg, Sweden
22th – 26th Aug 2016
Agenda item:7.1.4
Document for decision

## Slide 2: Proposal
When different numerologies are multiplexed with respect to the same reference numerology:
  OFDM symbol boundaries are aligned across different numerologies within the CP family (i.e., for a given CP overhead)
For any scaled numerology Fj = Fi*2M, in the case where Base numerology contains N symbols per ms and scaled numerology contains N*2M symbols per ms
  Each symbol length (including CP) of base numerology (w/ SCS = Fi) equals the sum of the corresponding 2M symbols of scaled numerology (w/ SCS = Fj)
  Each symbol may not necessarily be of the same length (e.g. in LTE numerology, symbol0 is long than symbol 1, 2, … 6)
  Multiple CP durations per each numerology is not precluded:
    For each CP family (NCP or ECP), each symbol length (including CP) of base numerology (w/ SCS = F0) equals the sum of the corresponding 2M symbols of scaled numerology (w/ SCS = Fs)

## Slide 3: Illustrations
Symbol alignment within a given reference numerology
Reference numerology SCS = 15kHz, N=7, NCP
Symbol is aligned at the boundary
15 kHz
30 kHz
60 kHz
7.5 kHz
0.5 ms
3.75 kHz