## Slide 1: WF on semi-open-loop transmission
Samsung, Nokia, ASB, ZTE, ZTE Microelectronics, CATT, KT…
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.3.1.1
R1-168055

## Slide 2: Background
Example: a CSI-process with K = 1 CSI-RS
Alt-1a: Transparent DMRS (i.e. DMRS and PDSCH precoded identically)
  PMI feedback points to one of N precoding hypotheses, where each precoding hypothesis corresponds to a set of M>1 precoding matrices on a subband
    PMI overhead log2(N) bits, where N can be 1
  Example:
    PRB-level or subcarrier(s)-level cycling of M precoders
    Cycling for a subset of codebook by Codebook-subset-restriction
    Cycling for i2, not for i1 (W1 reporting only for dual-stage codebook, e.g. Rel.10 8Tx, Rel.12 4Tx, Rel.13 Class A and its possible Rel.14 enhancements)
Alt-1b: Non-transparent DMRS (i.e. DMRS and PDSCH precoded differently)
  Received PDSCH signal as y = HW1W2s + n, where, S is unprecoded PDSCH, W2 refers to OL-precoding from L layer PDSCH to D DMRS ports, W1 refers to CL-precoding from DMRS/PDSCH to CSI-RS ports (or non-precoded channel)
  RI/PMI feedback: quantization of W1, based on H and knowledge of W2
  CQI feedback: quantization of HW1W2
  Example of W2 precoding (open-loop)
    Rank-1: SFBC (RE-level)
    Rank-2: LD-CDD or layer permutation

## Slide 3: Background
Example: a Class B CSI-process with K>1 CSI-RS
Alt-2a:
  A single wideband CRI report and/or long-term PMI
  Open-loop/semi-open-loop with K=1 is performed in the CSI-RS resource indicated by CRI
Alt-2b:
  CRI cycling, no CRI report
  open-loop/semi-open-loop with K=1 is performed in the corresponding CSI-RS resource indicated by CRI

## Slide 4: Background
Agreement
Confirm the working assumption of hybrid CSI
Further details on Mechanism 1
  Reporting content
    For the 1st eMIMO-Type (CLASS A), i1(1) and x-bit RI(1) are reported, while CQI(1) and i2(1) are not reported
      If UE supports up to 2 layers, x=0
      If UE supports up to 8 layer, x=1 where RI(1)={1, 3}
    For the 2nd eMIMO-Type (CLASS B K=1), CQI(2), PMI(2), RI(2) are reported
    Note: Superscript (y) represents the y-th eMIMO-Type, where y=1,2.
    FFS: Option for one eMIMO-Type to inherit RI reporting from another eMIMO-Type
  Working assumption: No inter-dependence between CSI calculations across two eMIMO-Types
  Reuse legacy CSI reporting mechanisms with the following refinement
  For PUCCH-based P-CSI
    Report i1(1) and RI(1) in one subframe
      FFS: Using either PUCCH format 2 or 3
    Periodicity of the CSI of 1st eMIMO-Type is an integer multiple of RI(2) periodicity of the 2nd eMIMO-Type.
    Subframe offset of the 1st eMIMO-Type is defined relative to RI(2) subframe offset of the 2nd eMIMO-Type.
      FFS: Whether subframe offset of the 1st eMIMO-Type can be fixed to 0
    Priority rule for collision handling is FFS.
  For PUSCH-based A-CSI
    FFS: what CSI(s) will be reported from UE when aperiodic CSI reporting is triggered
      Option 1: UE reports both CSI of 1st eMIMO-type and CSI of 2nd eMIMO-type.
      Option 2: UE reports either one of the 2 eMIMO-types.
    CSI encoding/mapping mechanisms is FFS.

## Slide 5: Proposal
Support both CLASS A and CLASS B with K≥1 CSI-RS resources for the eMIMO-Type of semi-open-loop
  For dual-stage codebook,
    RI, i1 and CQI reporting is supported for CLASS A and CLASS B with K=1
    CRI, RI, i1 and CQI reporting is supported for CLASS B with K>1
    Hybrid CSI-RS can be supported by using scheme 1
      For 1st eMIMO-Type, CSI reporting for scheme 1 is reused
      For 2nd eMIMO-Type, only CQI is reported
  For single-stage codebook with 2 and 4 ports (CLASS B with K≥1), CRI, RI and CQI are reported
Support RE level transmitter operation on PDSCH for both CSI reporting and PDSCH transmission
  FFS on the selection of transparent and/or non-transparent DMRS
  Down selection from the following transmission schemes in RAN1#87, including possible combination
    Precoder cycling
    Tx diversity
    LD-CDD
    Layer Permutation