## Slide 1: WF on alignment among different numerologies
LG Electronics, Qualcomm,
3GPP TSG RAN WG1 Meeting #86 R1-168090
Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda Item: 8.1.3.1

## Slide 2: Definition
For different numerology alignment, define the following two cases
  Inband case: different numerologies are multiplexed in the same NR carrier
  Outband case: different numerologies are not multiplexed in the same NR carrier

## Slide 3: Proposal
Symbol level alignment is assumed in the following cases
  Different subcarrier spacings with the same CP overhead in inband case
In other cases, symbol level alignment is not assumed.
  FFS: Slot/subframe level alignment for outband case

## Slide 4: Proposal
For normal CP family, choose one option from the followings for symbol-level alignment
  For Fs = F0 * 2n (n is a positive integer, F0 = 15 kHz),
    Each symbol length (including CP) of F0 equals the sum of the corresponding 2n symbols of Fs
    Option 1: The first 2n symbols of Fs have equal symbol length
    Option 2: Except for the first symbol of Fs , all symbols of Fs have equal symbol length. The length of first symbol of Fs is sum of length of the second symbol and 0.51 us
      Option 2-1. 0.51us can be reserved, and all symbols have the equal length

## Slide 5: Proposal
Symbol level alignment Option 1
Symbol level alignment Option 2

## Slide 6: Proposal
Symbol level alignment Option 2-1
Slot/subframe level alignment