## Slide 1: Way forward on DCI used for multiple SPS configurations
NTT DOCOMO, Huawei, HiSilicon, Panasonic, CMCC, ITRI,…
R1-168301
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016 Agenda item 7.2.2.4.1

## Slide 2: Background
In RAN1#84bis, it is agreed to support multiple SPS configurations for a given UE for eNB scheduling
  The eNB can dynamically trigger/release the different SPS-configurations by use of (E)PDCCH

## Slide 3: Observation
Event triggered traffic cannot be supported by SPS
Multiple SPS configurations should not require significant increase in the number of blind detection
In UL SPS, both explicit and implicit release are supported
  Contrary to UL SPS, eNB cannot be aware of status of sidelink transmissions. Therefore implicit release using empty transmissions cannot be supported for sidelink operation
  If a DCI for de-activation is miss-detected, UE may semi-persistently transmit in sidelink with unexpected resource allocation

## Slide 4: Proposal
Dynamic resource allocation is supported by eNB scheduling
  DCI format defined for V2V
A DCI for activation/release of sidelink SPS configurations is masked with SPS V2V-RNTI which is different from V2V-RNTI for dynamic scheduling

## Slide 5: Proposal for SPS
Multiple SPS configurations can be activated for an UE at same time.
SPS configuration index(es) is explicitly carried by the DCI
Both explicit release and implicit release of SPS configurations is supported
  More than one SPS configurations can be released by one DCI
  Explicit release is selected from following alternatives
    Alt. 1: Activation/release indicator in the DCI
      The activation/release indicator can be a combination of some field values in the DCI
    Alt. 2: A SPS configuration index reserved/configured for release
  Two implicit release is supported
    SPS configurations not indicated by the DCI for activation are assumed to be released
    An activated SPS configuration has a counter initialized at every activation. The SPS configuration is assumed to be active until the counter expires. The UE and eNB will release the SPS when the counter expires
    The UE indicates to the eNB when the SPS process is not needed anymore
      FFS how to indicate