## Slide 1: Way Forward on signaling design for MUST new DCI
Huawei, HiSilicon, Media Tek, China Telecom, NTT DOCOMO, LG Electronics […]
3GPP TSG RAN WG1 Meeting #86 R1-16xxxx
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item 7.2.5.2

## Slide 2: Background
In RAN1#85 some agreements were achieved
Agreement:
......
At least one new DCI is to be monitored by a UE once configured into MUST operation
  FFS on details
FFS MUST-near UE may assume MUST interference presence/absence is consistent among all of its scheduled PRBs for CRS-based TM and DMRS-based TM

## Slide 3: Proposal
For MUST operation Case 1 & 2 in TM2/3/4, a new DCI is introduced by extending the legacy DCI with the following information
  Interference existence
  FFS Power ratios
  FFS Separate encoding or joint encoding of interference existence and power ratios