## Slide 1: WF on CBR Measurement
Ericsson
3GPP TSG RAN WG1 Meeting #86 R1-168348
22nd – 26th August, 2016 Gothenburg, Sweden
Agenda item: 7.2.2.2.3

## Slide 2: Background
It is urgent to define the CBR measurement in order to contribute the ETSI harmonized standard for ITS

## Slide 3: Proposal
The sensing for determining CBR for LTE ITS is performed over a measuring interval of 100ms as follows:
  Each probe consists of measuring the signal PSD S over some PRBs over a single subframe
    SA probes: each probe includes a single SA subchannel
    Data probes: each probe includes a single data subchannel
    FFS: SLSS/PSBCH probes: each probe includes SLSS/PSBCH resources
    Wideband probes: each probe includes the system bandwidth
  The probe p is declared busy if S exceeds a pre-defined PSD threshold

## Slide 4: Proposal
Two CBR measurements are defined:
  Wideband CBR:
    The set includes all wideband probes in the last 100ms
  Frequency-selective CBR:
    The set includes all data, SA (FFS and SLSS/PSBCH probes) in the last 100ms
    FFS whether the probes set includes only the union of mode-2 pools, the union of mode-1 and mode-2 pools or all V2V subframes.
BW(p) is the bandwidth of probe p
B(p) is a binary variable indicating whether the probe p is detected as busy