## Slide 1
3GPP TSG-RAN1 Meeting #86 R1-168352
Gothenburg, Sweden 22nd - 26th August 2016
WF on NR UE Power Consumption Reduction
Qualcomm Incorporated
Agenda item: 8.1.3.2

## Slide 2: Background
Observation on LTE Days-of-Use(DoU)
  Legacy connected mode DRX design and typical parameter settings result in large percentage of power spent in the active state but decoding PDCCH only without any grant. [R1-166368]
Chart: YouTube (~3X)
| CDRX | Active: PDCCH-only | Active: Data
 | 2.2063 | 43.6954 | 29.703
Chart: Web-browsing (~2X)
| CDRX | Active: PDCCH-only | Active: Data
 | 3.4243 | 39.277 | 15.2429

## Slide 3: Proposal
Proposal 1: Impact of PDCCH-only UE decoding power consumption should be studied for DoU
Proposal 2: UE power reduction techniques in PDCCH-only slot should be studied
  E.g. PDCCH signal for low complexity decoding
  E.g. relaxed timing relationship between DL grant and DL data