## Slide 1: WF on UL DMRS Lengths
Nokia, Alcatel-Lucent Shanghai Bell, Huawei, HiSilicon, Qualcomm, CATT, Samsung
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, 22 – 26 August 2016
Agenda item: 7.2.4.1.3
R1-168369

## Slide 2: Background
Chairman note:
FFS during this week which new IFDMA sequence lengths (if any) shall be supported and designed
  If any new lengths larger than 36 are supported, the corresponding DMRS sequences are generated by the legacy mechanism by extension of a Zadoff-Chu sequence
Seq L | 1PRB | 2 | 3 | 4 | 5 | 6 | 8 | 9 | 10
RPF 2 | 6 | 12 | 18 | 24 | 30 | 36 | 48 | 54 | 60
RPF 4 | 3 | 6 | 9 | 12 | 15 | 18 | 24 | 27 | 30

## Slide 3: Proposal: IFDMA Sequence Design
For RFP=2,
  New lengths larger than 36 are supported. The corresponding DMRS sequences are generated by the legacy mechanism by extension of a Zadoff-Chu sequence.
  FFS: whether new lengths of 6, 18, 30 are supported