## Slide 1: WF on V2V priority signaling
Intel
3GPP TSG RAN WG1 Meeting #86 R1-168379
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 7.2.2.5

## Slide 2: Background (1/2)
At RAN1#84bis, the priority handling was agreed:
  Priority handling is supported over PC5 for eNB-scheduled and UE- autonomous V2V communication
  The priority information is taken into account in the resource (re)selection for UE-autonomous mode
    Further details are FFS
  Down-select between two alternatives at RAN1#85 meeting
    Alt.1 Priority information is signaled in SCI
    Alt.2 Priority information is not signaled in SCI

## Slide 3: Background (2/2)
At RAN1#85, further details of priority handling were discussed
Working Assumption:
  SCI explicitly includes priority information
    FFS how this priority information is exactly transmitted in SCI
    Priority information in a decoded SCI is used in resource (re)selection
    Priority information in a decoded SCI is not used as a condition to trigger resource reselection
    Priority information in a decoded SCI is not used as a condition to drop transmission

## Slide 4: Proposal
Priority of transmission is explicitly signaled in V2V SCI content (e.g. up to 3 bits)
Priority support and number of transmission priority levels is configurable
  Signaling details are up to RAN2 WG
  Up to 8 transmission priority levels can be configured
    Mapping between PPPP and transmission priority is decided by the RAN2 WG